Memorandum for: GOES Aerosol and Smoke Product (GASP) users

From: Shobha Kondragunta (Shobha.Kondragunta@noaa.gov) and Matthew Seybold (Matthew.Seybold@noaa.gov), co-leads for GASP, NOAA/NESDIS

Subject: Revisions to GOES Aerosol and Smoke Product (GASP) Algorithm

Date: January 7, 2009

Summary

This document describes the changes made to the GOES Aerosol and Smoke Product (GASP) algorithm and output file.  Changes include four parts: (1) bug fix related to the definition of relative azimuth angle, (2) procedure to calculate Aerosol Optical Depth (AOD) standard deviation, (3) addition of scattering angle information to the output file, and (4) new procedure to calculate surface reflectance.  Details of the changes and impact on the product are described below:

- Relative azimuth angle definition

An error related to the definition of relative azimuth angle in the GASP code was identified. In the original code, the relative azimuth angle is subtracted from 180o before it is used as a search index in the lookup table. The look-up table is, however, written in the reverse order of relative azimuth angle.  This resulted in wrong indexing in the look-up table and led to errors in surface reflectance retrieval and AOD retrieval. In the new code, this bug has been fixed.  Figure 1 shows an example of expected changes in the output.  For users of GASP binary files or imagery, the change will be transparent.  For users who run the GASP code, the errors in the following subroutines need to be fixed:

GOES-WEST:

In the program named as “goes10.pro”, both on line 2127 and 3551:

Originally it is written as:

pazi = 180. – pazi

Change made:

delete this line

GOES-EAST:

In program named as “goes12.pro”, both on line 2158 and 3608:

Originally it is written as:

pazi = 180. – pazi

Change made:

delete this line

(2) AOD standard deviation

AOD standard deviation is one of the parameters used to screen cloud contaminated AOD values.  In the IDL reader (Appendix A) used to read GASP binary files, pixels with AOD standard deviations > 0.3 are flagged as bad data.  The procedure to calculate AOD standard deviation has been modified from the original method.  In the original method, AOD standard deviation was calculated in a 3 X 3 box for all pixels, without checking if any of the 9 pixels in this 3 X 3 box are cloudy. Not checking if a pixel is cloud-free or not resulted in high AOD standard deviation, when some of the pixels in the 3 X 3 box are contaminated by clouds.  In the new method, AOD standard deviation is calculated using a 5 X 5 box but only for pixels which are identified as clear by the cloud mask, and the number of valid (cloud-free) pixels in the box is greater than 10.  Otherwise AOD in this central pixel is considered as invalid. This change will also be transparent to the users.

Figure 2 shows an example of original operational GOES-12 AOD retrievals compared to retrievals with new AOD standard deviation calculation.

(3) Addition of scattering angle to the output file

Research work has also shown that AOD retrievals are very sensitive to scattering angle and for certain scattering angle range (backward scattering), sensitivity to AOD changes is poor and thus retrievals are not very accurate.  Based on various tests including AERONET comparisons, we noticed that AOD retrievals are accurate for scattering angles between 50o and 170o. Figure 3 shows an example of GASP output with and without scattering angle based screening. However, this screening is very tight and reduces the data coverage for certain locations and times of the day.  Instead of screening the data for users, we decided to provide all data but also provide scattering angle information in the output files so users can use their discretion in using the data.  Scattering angle is written out as a parameter in the GASP binary output files that have an extension of ‘.all’ in the filename. For historic data files that do not have scattering angle information, it can be easily computed using the code provided below (Appendix B).  We recommend not using AOD data for scattering angles less than 50o and greater than 170o.

(4) Surface reflectance calculation

In the original approach, clear sky composite is created using counts in channel 1.  For any given day, 2nd darkest pixel (in units of counts) in the previous 28 days including current day, is used to compute surface reflectance.  In converting counts to surface reflectance, solar zenith angle corresponding to the day for which AOD is being calculated is used.  This approach creates a large artifact in the early morning and late evening since changes of solar zenith angle during the 28 days can be large, especially in the Spring and the Fall.  In the new approach, surface reflectance is retrieved for every day assuming a background aerosol optical depth of 0.02 and a search is made for the 2nd darkest pixel (in surface reflectance) in the previous 28 days including current day.  This improves the surface reflectance retrieval because the correct solar zenith angle is used.

Figure 1: GOES-12 original processing (left panel) and processing with azimuth angle bug fix (right panel)

Figure 2: GOES-11 data with old AOD standard deviation (left panel) and new AOD standard deviation (right panel)

Figure 3: GOES-11 processing with no scattering angle based screening (left panel) and with scattering angle based screening (right panel)

Appendix A: IDL Reader to read GASP binary file

function rd_aod_all,bcld=bcld,bad=bad,bcls=bcls,glat=glat,glon=glon,$

dsn=dsn,dir=dir,bsfc=bsfc,bmos=bmos,bmsk=bmsk,bch1=bch1,bsig=bsig,$

baodstd=baodstd,bsca=bsca,nsat=nsat,nx=nx,ny=ny,good=good

nfiles=1

for i=0,nfiles-1 do begin

print,nx,ny

;    f1=dir+dsn

f1=dsn

;read in data

baod = bytarr(nx,ny)

bcls = bytarr(nx,ny)

baodstd=baod

bsfc = baod

bch1 = bsfc

bmos = bsfc

bcld = bsfc

bsig = bsfc

bmsk = bsfc

bcls = bsfc

bsca = bsfc

print,f1

openr,ilun,f1,/comp,/get_lun

readu,ilun,baod,bmsk,bcls,baodstd,bsfc,bch1,bmos,bcld,bsig,bsca

;check,baod

free_lun,ilun

cc=where(baod eq 0)

dd=where(baod eq 255)

baod = float(baod) / 100. - 0.5

;    printf,2,baod

;    close,2

baodstd = float(baodstd) / 100.

bsfc = float(bsfc) / 500. - .1

bch1 = float(bch1) / 600.

bmos = float(bmos) / 600.

bsig = float(bsig) / 250.- 0.5

bsca = float(bsca)

;    newmask = bytarr(nx,ny)

; Note: here selection criteria may change based on user preference

; Normal  criteria

good = where(baodstd lt 0.3 and bsig gt 0.01 and bsfc lt 0.15 and bsfc gt 0.005 $

and bcls gt 15 and baod lt 10.and bch1 gt 0. and bcld eq 1 and bsca gt 70 and bsca lt 170, $

ngood,compl=bad,ncomp=nbad)

;    good = where(bsfc lt 0.15 and bsfc gt 0.005 $

;      and baod lt 10.and bch1 gt 0. and bcld eq 1, $

;      ngood,compl=bad,ncomp=nbad)

; A little strict criteria

;    good = where(baodstd lt 0.15 and bsig gt 0.01 and bsfc lt 0.15 and bsfc gt 0.005 $

;      and bcls ge 25 and baod lt 10.and bch1 gt 0. and bcld eq 1, $

;      ngood,compl=bad,ncomp=nbad)

baod(bad)=-999.9

bch1(bad)=-999.9

;bsfc(bad)=-999.9

;bcld(bad)=-999.9

;bcls(bad)=-999.9

endfor

return,baod

stop

end

Appendix B:  Subroutine to calculate the scattering angle

An IDL subroutine to calculate the viewing geometry for both GOES-EAST and WEST satellite is attached. Besides the scattering angle, this subroutine also calculates solar zenith angle, solar azimuth angle, satellite viewing zenith angle, satellite azimuth angle and relative (solar - satellite) azimuth angle. The required inputs for this subroutines are as follow:

jday  – the day of the year

time  – UTC time of the observation in the format of “HHMMSS”. HH  is the hour, MM is the minutes and SS is the second.

npixel  – number of pixel for each scanline:

GOES-EAST:  2000

GOES-WEST: 2500

nlines  – number of scanline

GOES-EAST: 850

GOES-WEST: 912

Sat_lat  –  latitude of subsatellite point

GOES-EAST: 0

GOES-WEST: 0

Sat_lon  –  longitude of subsatellite point

GOES-EAST: -75

GOES-WEST: -135

lat_geo  –  array of latitude

lon_geo –  array of longitude

The corresponding outputs are listed as follow:

solzen –  solar zenith angle

az_not –  solar azimuth angle

theta  –  satellite viewing zenith angle

azimuth –  satellite azimuth angle

sca_ang  –  scattering angle

imgazi – relative azimuth angle

the relative azimuth angle is defined as solar azimuth angle minus satellite azimuth angle and in the range of 0 to 180.

pro goes_gasp_geometry,  $ jday,time,solzen,az_not,theta,azimuth,sca_ang,imgazi,lat_geo,lon_geo,npixel,nlines, $

sat_lat, sat_lon

; ========input============

;     jday  – the day of the year

;     time  – UTC time of the observation in the format of “HHMMSS”. HH is the hour,

;                 MM is the minutes and SS is the second.

;   npixel  – number of pixel for each scanline: 2000 (GOES-EAST), 2500 (GOES-WEST)

;   nlines  – number of scanline. 850 (GOES-EAST), 800 (GOES-WEST)

; lat_geo  –  array of latitude

; lon_geo –  array of longitude

; ========output============

;    solzen –  solar zenith angle

;    az_not –  solar azimuth angle

;      theta  –  satellite viewing zenith angle

;  azimuth –  satellite azimuth angle

; sca_ang  –  scattering angle

;    imgazi – relative azimuth angle

imgnx=npixel

imgny=nlines

pi = !pi

dtor = !pi / 180.

lat = fltarr(imgnx,imgny)

lon = fltarr(imgnx,imgny)

lat=lat_geo

lon=lon_geo

rlat=0

rlon = 0

satlat = sat_lat

satlon = sat_lon

;--------------------------------

;  calculate solar  angle :

;!   solzen - solar zenith angle

;!   az_not - solar azimuth angle

HH  = fix( FLOAT(TIME) / 10000.0)

MM = fix((FLOAT(TIME)/100) - FLOAT(HH) * 100)

SS = TIME - HH * 10000L - MM * 100L

tu = FLOAT(HH) + FLOAT(MM)/60.0 + FLOAT(SS)/3600.0

pi = !pi

rad = !pi / 180.

glat = satlat

glon = satlon

HH = fix( FLOAT(TIME) / 10000.0)

MM = fix((FLOAT(TIME)/100) - FLOAT(HH) * 100)

SS = TIME - HH * 10000l - MM * 100l

DTIME = FLOAT(HH) + FLOAT(MM)/60.0 + FLOAT(SS)/3600.0

H_ANG = -1.0 * PI * (DTIME-12.0) / 12.0

nc = 0

nd = 0

DECLIN = -23.45 * COS(FLOAT(jday)*2.*PI/365. + 10.*2.*PI/365.)

na = where(lat ge -90. and lat le 90. and lat gt declin,na,$

complement=b,ncomplement=nb)

gd = where(lat ge -90. and lat le 90.) ;,complement=ng)

g=gd

betaa=lat

azimuth=lat

betaa(*)=0.

mu_not = lat

mu_not(*,*)=0.

gd = where(lat ge -90. and lat le 90.) ;,complement=ng)

ng = where(lat lt -90. or lat gt 90.) ;,complement=ng)

MU_NOT(gd) = (SIN(LAT(gd)*RAD)*SIN(DECLIN*RAD) + $

COS(LAT(gd)*RAD)*COS(DECLIN*RAD)*COS(H_ANG-LON(gd)*RAD))

solzen = acos(mu_not < 1.) / rad

mu_not = 0

nc = 0

nd = 0

a = 0

;  CALCULAT SATELLITE ZENITH ANGLE

betaa=lat

theta=lat

betaa(*)=0.

betaa(g) = ACOS(COS(LAT(g)*RAD) * COS((GLON - LON(g))*RAD))

theta(g) = asin((42164.*sin(betaa(g)) / $

sqrt(1.8084e9 - 5.3725e8*cos(betaa(g)))) < 1) / rad

;!      CALCULATE SOLAR AZIMUTH (gasp)

a = where(lat ge -90. and lat le 90. and lat gt declin,na,$

complement=b,ncomplement=nb)

g=gd

gd = 0

az_not = lat

az_not(*,*) = 0.

if (na gt 0) then az_not(a) = ACOS( COS((LAT(a)-DECLIN)*RAD) * COS(H_ANG-LON(a)*RAD))

if (nb gt 0) then az_not(b) = ACOS( COS((LAT(b)-DECLIN)*RAD) * $

COS(LON(b)*RAD-H_ANG))

if (na gt 0) then AZ_NOT(a) = SIN(H_ANG-LON(a)*RAD) / SIN(az_not(a))

if (nb gt 0) then AZ_NOT(b) = SIN(LON(b)*RAD-H_ANG) / SIN(az_not(b))

az_not(g) = (az_not(g) > (-1.)) < 1.

AZ_NOT(g) = ASIN( AZ_NOT(g) )

if (na gt 0) then AZ_NOT(a) = PI - AZ_NOT(a)

if (nb gt 0) then AZ_NOT(b) = PI + AZ_NOT(b)

AZ_NOT(g) = AZ_NOT(g) /RAD

nc = 0

nd = 0

a = 0

if (nb gt 0) then c = where(az_not(b) lt 180.,nc,complement=d,ncomplement=nd)

if (nc gt 0) then az_not(b(c)) = 180. - az_not(b(c))

if (nd gt 0) then az_not(b(d)) = 540. - az_not(b(d))

;!      CALCULATE THE SATELLITE AZIMUTH (GASP)

betaa=lat

betaa(*)=0.

betaa(g) = ACOS(COS(LAT(g)*RAD) * COS((GLON - LON(g))*RAD))

a = where(lat gt (-90) and lat le 90. and lat gt glat,na,$

complement=b,ncomplement=nb)

azimuth=lat

azimuth(*,*)=0.

if (na gt 0) then AZIMUTH(a) = SIN((GLON-LON(a))*RAD) / SIN(BETAa(a))

if (nb gt 0) then AZIMUTH(b) = SIN((LON(b)-GLON)*RAD) / SIN(BETAa(b))

azimuth(g) = (azimuth(g) > (-1.)) < 1.

azimuth(g) = asin(azimuth(g))

if (na gt 0) then azimuth(a) = pi - azimuth(a)

a = 0

if (b(0) ge 0) then azimuth(b) = pi + azimuth(b)

azimuth(g) = azimuth(g) / rad

if (nb gt 0) then c = where(azimuth(b) lt 180.,nc)

if (nb gt 0) then d = where(azimuth(b) ge 180.,nd)

if (nb gt 0 and nc gt 0) then azimuth(b(c)) = 180. - azimuth(b(c))

if (nb gt 0 and nd gt 0) then azimuth(b(d)) = 540. - azimuth(b(d))

imgsza=solzen

imgvza=theta

imgazi=(az_not-azimuth)

idx1=where (imgazi lt 0.,n1)

if (n1 gt 0 ) then  imgazi(idx1)=imgazi(idx1)+2.*pi

idx2=where (imgazi gt (2.*pi),n2)

if (n2 gt 0 ) then  imgazi(idx2)=imgazi(idx2)-2.*pi

rad = dtor

cosga =-cos(imgsza*rad)*cos(imgvza*rad) -sin(imgsza*rad)*sin(imgvza*rad)*cos(imgazi*rad)

cosga = (cosga > (-1.)) < 1.

sca_ang=acos(cosga) / rad

end