GOES EVAPOTRASPIRATION (ET) AND

DROUGHT PRODUCT SYSTEM (GET-D),  version 1.0

# Interface Control Document

(Documentation Version 1.7)

December 2015

Prepared for:

National Environmental Satellite, Data, and Information Service,

Office of Satellite Data Processing and Distribution

Prepared by:

Zhengpeng Li, ESSIC/UMD/CICS

for

NOAA/NESDIS/STAR

College Park, MD 20740

Last Revision: December 2015

# Summary of Changes:

07/26/2015 – Z. Li,

First version

10/26/2015 – Z. Li,

2nd version after the System Readiness Review

12/04/2015– Z. Li,

3rd version for the Operational Readiness Review.

Table of Contents

Interface Control Document	1

Summary of Changes:	2

1.0 INPUT FILES	5

1.1 Processing Scripts / Configuration Files	5

1.2 Climate Forecast System (CFS) Forecast Fields	8

1.3 GOES Imager Area Files	10

1.4 GOES Surface and Insolation Products (GSIP)	11

1.5 Visible Infrared Imaging Radiometer Suite (VIIRS)	12

1.6 Interactive Multisensor Snow & Ice Mapping System (IMS) Snow and Ice Coverage (IMS Snow)	12

2.0 INTERMEDIATE FILES	13

2.1 Meteorological intermediate files	13

2.2	GOES Imager Area Files	15

2.3 GSIP Files	16

2.4 VIIRS Files	16

2.5 Snow Mask Files	16

2.6 ET and ESI files	17

3.0 OUTPUT FILES	17

3.1 Direct Access Binary Data	18

3.2 GRIB Edition 2 (GRIB2) messages	18

3.3 Network Common Data Format (netCDF) Data	19

3.4 Portable Network Graphics (PNG) Image Files	19

4.0 ANCILLARY FILES	20

4.1 Static files used for CFS processing	20

4.2 Static files used for GOES data processing	20

4.3 Static files used for GSIP processing	21

4.4 Static files used for VIIRS processing	21

4.5 Static files used for snow mask processing	22

4.6 Static files used for ET/ESI processing	22

Reference	23

This interface control document contains information on the GOES evapotraspiration (ET) and drought product system (GET-D) input products (i.e., dynamic inputs), intermediate products, output products, and static ancillary input files. In addition, information on servers from which inputs are downloaded is contained in this document.

Information on installing and compiling the GET-D system, along with system monitoring, recovery of processing failures, and long-term maintenance, may be found in the GET-D System Maintenance Manual.

The system description document (SDD) contains information on the GOES Surface and Insolation Products (GET-D) data processing system - GET-D application, GET-D input and output products, the system operating environment, system processes, and system programs.

# 1.0 INPUT FILES

The GET-D system utilizes five types of dynamic input files:  Imager channel data from GOES, Insolation data from GSIP L2 product, daily input GIMGO and IVISR granules from VIIRS, Climate Forecast System (CFS) forecast data, and Interactive Multisensor Snow & Ice Mapping System (IMS) snow and ice coverage data (Table 1.1).

Dynamic inputs are distinguished from static ancillary inputs.  The dynamic inputs (described in this section) contain temporally changing data values and are downloaded from external sources on a routine basis.  In contrast, the static (or ancillary) inputs do not change, are kept on the system in the data/static/ directory, and are described in Section 4.0 of this document.

## 1.1 Processing Scripts / Configuration Files

The GET-D system uses CSHELL scripts to setup the processing parameters and passed to the executables directly. There are multiple configuration files used in the processing scripts that also used to control inputs/outputs. When CSHELL scripts change, configuration control files also need to be updated to make sure the process works properly.

Table 1.1 GET-D external inputs

| Item | Type | Source | Data Type | Description |
| --- | --- | --- | --- | --- |
| CFS | 6-hour Input + 3-hour forecast | NCEP ftp server | GRIB2 files | Forecast data from the NOAA/NCEP Climate Forecast System (CFS) |
| GENHEM | Hourly Input | SATEPSDIST2e NSOF server | AREA files | GOES-EAST Northern Hemisphere sector scan, channels 1, 2, 4 |
| GWNHEM | Hourly Input | SATEPSDIST3e NSOF server | AREA files | GOES-WEST Northern Hemisphere sector scan, channels 1, 2, 4 |
| GSIP EAST | Hourly Input | SATEPSDIST3e NSOF server | NETCDF4 | GSIP L2 product |
| GSIP WEST | Hourly Input | SATEPSDIST3e NSOF server | NETCDF4 | GSIP L2 product |
| VIIRS | Daly-hour Input | SATEPSDIST3e NSOF server | HDF5 | VIIRS spectral reflectance data |
| IMS Snow | Daily Input | SATEPSDIST1e NSOF server | ASCII files | Interactive Multisensor Snow & Ice Mapping System (IMS) snow and ice coverage |

Table 1.2 GET-D CSHELL scripts and configuration file inputs

| Name | Usage | Configuration files |
| --- | --- | --- |
| run_daily_SUNTIMES.csh | compute the two morning times for the NA domain | sunrise8km_local.cfg |
| run_daily_CFS_STEP1.csh | Process 3 hours CFS data in GRIB2 format into 24 hours meteorological variables in plain binary format. | GETD_CFS_STEP1.cfg CFSR.cfg |
| run_daily_CFS_STEP2.csh | Extract morning meteorological variables from 24 hours data. | GETD_CFS_STEP2_8km.cfg |
| run_daily_GOES_IDL.csh | Convert the GOES micada files into plain binary data files by running the IDL scripts. | N/A |
| run_daily_GOES_STEP1.csh | Convert the hourly GOES raw data into hourly brightness temperature and apply the cloud mask | GOES_EAST.cfg |
|  |  | GOES_WEST.cfg |
| run_daily_GOES_STEP2.csh | Run the ATMOSPHERIC correction | ATMO_EAST8km.cfg |
|  |  | ATMO_WEST8km.cfg |
| run_daily_GOES_STEP3.csh | Combines the GOES EAST and WEST into NA domain | GETD_combine_GOES8km.cfg |
| run_daily_GSIP_STEP1_2.csh | Remap GSIP EAST from NETCDF to binary for each hour | GSIP_EAST_NA.cfg |
|  | Remap GSIP WEST from NETCDF to binary for each hour | GSIP_WEST_NA.cfg |
|  | Combine EAST and WEST for each hour. | GETD_combine_GSIP8km.cfg |
|  | Combine 24 hourly data into one daily file | GSIP_step2_NA.cfg |
| run_daily_GSIP_STEP3.csh | Extract the GSIP data into 24 hours local time using two days GSIP inputs in UTC time. | GSIP_step3_NA.cfg |
| run_daily_aggEVI.csh | Run the EVI aggregation process using GVF EVI inputs. | EVI_temp.para |
| run_daily_VIIRS_EVI.csh | Extract the VIIRS EVI data into NA 8km domain from global domain. | VEVI_global1km.cfg |
| run_daily_VIIRS_LAI.csh | Compute the VIIRS EVI data into LAI using regression parameters. | LAI_na8km.cfg |
| run_daily_SNOWMASK.csh | Processing the snow mask data from ascii file into plain binary data | snow24km_8km.cfg |
| run_VLAI_ALEXI.csh | Run the ALEXI model to compute the ET | GETD_NA_8km_VLAI.cfg |
| run_daily_ESI_compute.csh | Calculate the fraction of Potential ET (fPET) using ET results from ALEXI and reference ET computed in GETD | ESI_refET8km.cfg |
| run_daily_ESI_smooth.csh | Run the ESI smoothing procedure for daily fPET outputs using historical fPET results. | smooth_VLAI_ESI8km.cfg |
| run_daily_ESI_composite.csh | Calculate the daily fPET into weekly composited fPET, and calculate the ESI for 2, 4, 8, 12 weeks. | GETD_composite_ESI8km.cfg |
| run_gen_images_not_validated.csh | Generate the images for the 2, 4, 8, 12 weeks ESI. | N/A |
| run_daily_GETD_pack.csh | Pack the daily fluxes outputs into GRIB2 and NETCDF files. | GETD_pack_8km.cfg |

## 1.2 Climate Forecast System (CFS) Forecast Fields

Forecast data from the NOAA/NCEP Climate Forecast System (CFS) are used to supply primary meteorological inputs to the GET-D system.  These inputs are air temperature, specific humidity, geopotential height, surface wind speed and downwelling longwave radiation.  The data used by GET-D are the 00 hour and the 03 hour forecast.  The CFS data are at 0.5 degree spatial resolution. Two scripts are used to process the input CFS data:

- run_daily_CFS_STEP1.csh: extract the meteorological variables from GRIB2 input files into binary data in UTC time.

- run_daily_CFS_STEP2.csh: extract meteorological variables for two morning times and 24 hours at local time in the North America domain.

Two days of CFS data are used for each GET-D daily run to provide local 24 hours daily information for the North America domain. Each day, 4 files at UTC hours 00, 06, 12 and 18 with 6 hours interval, and 4 03 hour forecast files are used to interpolate into hourly information for the GET-D run.

CFS data are downloaded by the GET-D system at UTC hours 01 for the previous day’s 3-hour data.  The GET-D run after all the in 6-hour cycles for times 00, 06, 12, and 18 UTC.  The following table shows the time of GET-D download and CFS model cycle, and the time represented by the data.

Table 1.3 CFS data for a single day.

| CFS model cycle downloaded (UTC) | Forecast (hours) | Example file |
| --- | --- | --- |
| 00 | 03 | CFSR_20150624_0000_000.grb2 CFSR_20150624_0000_003.grb2 |
| 06 | 09 | CFSR_20150624_0600_000.grb2 CFSR_20150624_0600_003.grb2 |
| 12 | 15 | CFSR_20150624_1200_000.grb2 CFSR_20150624_1200_003.grb2 |
| 18 | 21 | CFSR_20150624_1800_000.grb2 CFSR_20150624_1800_003.grb2 |

Notice that the GET-D processing run should start after all the 8 data files are downloaded for a single day and before the GOES Imager data processing.  This is not a problem because the GET-D processing is daily based.

The CFS pre-processing script, CFS_download.csh, downloads the CFS files from the NCEP FTP server:

ftpprd.ncep.noaa.gov

The files from NCEP are in GRIB2 format.  The file names are of the form:

CFSR_20150624_0000_000.grb2

CFSR_20150624_0000_003.grb2

CFSR_YYYYMMDD_HHHH_PPP.grb2

where “YYYY” is the year, “MM” is the month in two digits, “DD” is the day in the month in two digits, and “HHHH” is the CFS model cycle (0000, 0600, 1200, or 1800) and “PPP” indicates the forecast hours, range from 000 to 003.  Data are typically available on the NCEP server for 24-30 hours.

The CFS data are required for the GET-D algorithms to compute the ET, but are also used in the atmospheric correction of the GOES radiance data.  Without CFS data, the GET-D system will not run (and a failure message is sent to operations personnel).

## 1.3 GOES Imager Area Files

The Imager Area files are obtained from the ADDE server using McIDAS (Man-Computer Interactive Data Access System) software.  There are 4 processing scripts to process the GOES imager area files into model inputs:

- run_daily_GOES_IDL.csh: convert the area files into channel files for GOES EAST and WEST.

- run_daily_GOES_STEP1.csh: convert the channel data files into surface radiance for GOES EAST and WEST.

- run_daily_GOES_STEP2.csh: convert the surface radiance into land surface temperature with atmospheric correction for GOES EAST and WEST.

- run_daily_GOES_STEP3.csh: extract the land surface temperature for North American domain from GOES EAST and WEST.

The scripts are oriented to data input from NOAA/OSPO servers, where satellite data are channel-separated. When all the channel-separated Area files are downloaded, the scripts are executed to produce the land surface temperature inputs for the model.

McIDAS is also used to alter the spatial resolution of the channel-1 files from one-km visible-channel spatial resolution to four-times lower spatial resolution of 1, 2, and 4 channels used in GET-D (4 km).  In the GET-D processing system, all input GOES Area files are at 4km spatial resolution but will be resample to 8km in step 3.

Table 1.4 GOES McIDAS  data for a single day.

| GOES satellite | BANDS | Example |
| --- | --- | --- |
| GOES 13 EAST | 01 | goes13.2015.215.211519.BAND_01 |
| GOES 13 EAST | 02 | goes13.2015.215.211519.BAND_02 |
| GOES 13 EAST | 04 | goes13.2015.215.211519.BAND_04 |
| GOES 15 WEST | 01 | goes15.2015.215.223019.BAND_01 |
| GOES 15 WEST | 02 | goes15.2015.215.223019.BAND_02 |
| GOES 15 WEST | 04 | goes15.2015.215.223019.BAND_04 |

Upon download, the Area files are renamed by the GET-D processing script, download_daily_GOES.csh, and copied to the appropriate subdirectory in the GOES_IMAGER directory.  The Area filenames have the following convention:

AREA_DDDDDD_N_YYYYJJJJ_HHMM

where	DDDDDD 	= domain (GEDISK, GENHEM, GWDISK, 								      GWNHEM, MSGFD, MTSFD)

N		= channel number

YYYY		= year

JJJ		= day of year

HH		= hour

MM		= minute

IDL routines are used to read the Area files.  These routines are in the source code file IDL.

## 1.4 GOES Surface and Insolation Products (GSIP)

The GSIP data provided the insolation data for GET-D ET estimates.

Two scripts are used to process the input GSIP data:

- run_daily_ GSIP_STEP1_2.csh: extract the insolation variables from GSIP L2 NETCDF input files into binary data in UTC time.

- run_daily_CFS_STEP3.csh: extract the local insolation data for 24 hours at local time in the North America domain.

Table 1.5 GSIP data for a single day.

| GOES satellite | Hours | Example |
| --- | --- | --- |
| GOES 13 EAST | 0045 ….. 2345 | gsipL2_goes13_GENHEM_2015335_0145.nc.gz gsipL2_goes13_GENHEM_2015335_2345.nc.gz |
| GOES 15 WEST | 0000 ….. 2300 | gsipL2_goes15_GWNHEM_2015335_0000.nc.gz gsipL2_goes15_GWNHEM_2015335_2300.nc.gz |

## 1.5 Visible Infrared Imaging Radiometer Suite (VIIRS)

The reflectance data from VIIRS provided the vegetation dynamic input for GET-D system. Three scripts are used to process the input VIIRS data into LAI:

- run_daily_aggEVI.csh: Aggregate the EVI granule data in HDF5 format into global EVI binary file.

- run_daily_VIIRS_EVI.csh: extract the EVI in the North America domain from global EVI binary file.

- run_daily_VIIRS_LAI.csh: use the regression parameters to compute the LAI from EVI input in the North America domain.

The input file format is:

GVF-EVI_s20151012_e20151018_h19v06_c201510200318110.h5

## 1.6 Interactive Multisensor Snow & Ice Mapping System (IMS) Snow and Ice Coverage (IMS Snow)

Snow coverage data from the Interactive Multisensor Snow & Ice Mapping System (IMS) are used by GET-D to provide snow.  IMS Snow data are available at 24km spatial resolution (in a polar stereographic grid), which is then remapped in the GET-D snow pre-processing step to 1/8 degree spatial resolution (in the GET-D cylindrical equidistant latitude-longitude grid). After that, it is remapped onto the Imager pixels (improvement of the snow processing is planned for the next versions of GET-D).

Snow data are downloaded once per day from NOAA/NESDIS/OSDPD from the server:

satepsdist1e.nesdis.noaa.gov

IMS Snow data downloaded are in ASCII format.  The GET-D snow pre-processing step runs the GET-D program with option “, snowims.f90, which reads the ASCII data, regrids the snow data (as described above), and outputs binary format snow data.  Data reside on the OSDPD server for roughly 5 days.

run_daily_SNOWMASK.csh

Files downloaded have the filename imsYYYYJJJ.asc, where YYYY is the year and JJJ is the day-of-year.  Files after the GET-D snow pre-processing have the name GET-D_YYYY_JJJ_imsnw.grd, where YYYY is the year and JJJ is the day-of-year.  Both files are stored in the /snow_files directory.

The IMS Snow data is required by the GET-D system to mask out the pixels in the ET estimates.

# 2.0 INTERMEDIATE FILES

GET-D v.1.0 creates intermediate files during the process. The intermediate files are located under ‘data’ directory and can be used for debugging purpose.

## 2.1 Meteorological intermediate files

Upon download, the CFS processing script, run_daily_CFS_STEP1.csh will be run to generate the climate variables in common grid in 24 hours UTC time. The output filenames are listed as follows:

Table 2.1 CFS data extracted for a single day in UTC time.

| File name | Description | Notes |
| --- | --- | --- |
| pot_profile.bin | Morning potential temperature at each height level | Used for atmospheric correction for GOES radiance data |
| temp_profile.bin | Morning temperature at each height level | Used to compute the potential temperature in the morning for ALEXI model |
| pressure_profile.bin | Morning temperature at each height level | Used to compute the potential temperature in the morning for ALEXI model |
| spfh_profile.bin | Specific humidity at each height level | Used to compute the potential temperature in the morning for ALEXI model |
| height_profile.bin | Height levels from the surface | Used to compute the potential temperature in the morning for ALEXI model |
| psfc_series.bin | Surface pressure at 24 hours UTC | Used to extract the two morning pressures for ALEXI model inputs |
| q2_series.bin | Surface specific humidity at 24 hours UTC | Used to extract the two morning air humidity for ALEXI model inputs |
| t2_series.bin | Surface air temperature at 24 hours UTC | Used to extract the two morning air temperature for ALEXI model inputs |
| wind_surface.bin | Surface wind speed at 24 hours UTC | Used to extract the two morning wind speed for ALEXI model inputs |
| lwdn.bin | Surface long wave down radiation at 24 hours UTC | Used to extract the two morning long wave down radiation for ALEXI model inputs |
| sun_rise15.bin | Morning sun rise time | Used to extract the morning profile |

These files are stored in the $data/CFS_COMMON subdirectory with the directory name: $data/CFS_COMMON/YYYYDDD

where “YYYY” is the year, “DD” is the day of the year in three digits, ranges from 001 to 366 (leap year).

## GOES Imager Area Files

The intermediate files generated in GOES data processing is listed in the following table.

Table 2.2 GOES intermediate data in a single day in UTC time.

| GOES satellite | Data file | Example |
| --- | --- | --- |
| GOES 13 EAST $HOME/data/TRAD/EAST | trad1.dat trad2.dat | Brightness temperature in GOES EAST domain at two morning times. |
| GOES 15 WEST $HOME/data/TRAD/WEST | trad1.dat trad2.dat | Brightness temperature in GOES WEST domain at two morning times. |
| GOES 13 EAST $HOME/data/LST/EAST | lst1.dat lst2.dat | Land surface temperature in GOES EAST domain at two morning times. |
| GOES 15 WEST $HOME/data/LST/WEST | lst1.dat lst2.dat | Land surface temperature in GOES WEST domain at two morning times. |
| data/ALEXI_LST | lst15 lst55 | Land surface temperature in NA domain at two morning times. |

## 2.3 GSIP Files

The intermediate files generated in GSIP data processing is listed in the following table.

Table 2.3 GSIP intermediate data in a single day in UTC time.

| Directory | Data file | Example |
| --- | --- | --- |
| $HOME/data/ GSIP/UTP | inso_na_24h_2015291.dat | 24 hours UTC time insolation data extracted from GSIP L2 data in North American domain. |
| $HOME/data/ ALEXI_MET/[yyyyddd] | inso_24h | Contains the 24 hours local time insolation data extracted from two UTC days insolation data |

## 2.4 VIIRS Files

The intermediate files generated in VIIRS data processing is listed in the following table.

Table 2.4 VIIRS intermediate data files.

| Directory | Example data file | Example |
| --- | --- | --- |
| $HOME/data/weekly_evi/[yyyyddd]/ | GVF-WKL-GLB_v1r0_npp_s20151001_ e20151007_c201510132242180.dat | Global EVI binary data |
| $HOME/data/EVI | VEVI_NA8km_2015289.dat | The EVI data in North American domain |
| $HOME/data/ ALEXI_LAI/[yyyyddd] | VLAI | The LAI data in North American domain |

## 2.5 Snow Mask Files

The intermediate files generated in snow mask data processing is listed in the following table.

Table 2.5 snow mask intermediate data files.

| Directory | Example data file | Notes |
| --- | --- | --- |
| $HOME/run | ims_col8km_test.dat | Col index used for snow mask |
| $HOME/run | ims_row8km_test.dat | Row index used for snow mask |
| $HOME/data/ALEXI_SNOW/[yyyyddd] | snow_mask | Daily snow mask. |

## 2.6 ET and ESI files

The intermediate files generated in ESI data processing is listed in the following table.

Table 2.6 ESI intermediate data files.

| Directory | Example data file | Notes |
| --- | --- | --- |
| $HOME/data/esi/[yyyyddd]/ | XLE2.bin | Daily ET in the morning |
| $HOME/data/esi/[yyyyddd]/ | REF_ET.bin | Daily reference ET in the morning |
| $HOME/data/esi/[yyyyddd]/ | ESI.bin | Daily fraction of ET and reference ET in the morning |
| $HOME/data/esi/[yyyyddd]/ | FPPM_SMN365.bin | Smoothed daily ESI |
| $HOME/data/esi/[yyyyddd]/ | ESI_1week.bin | Composite weekly ESI |

# 3.0 OUTPUT FILES

GET-D outputs are generated for each day:

- Daily ET and fluxes.

- Daily ESI 2, 4, 8, 12 weekly composite.

The GET-D system generates four types of output files: direct access binary data, Hierarchical Data Format (HDF-4) data, Network Common Data Format (netCDF-3) data, and Portable Network Graphics (PNG) images.

## 3.1 Direct Access Binary Data

- GET-D binary data files contain daily fluxes and QC flags for each day under data/ET/[yyyyddd]  directory with year and day of the year information:

Table 3.1:  GET-D Output products

| File Name | Description | Units |
| --- | --- | --- |
| EDAY.bin | Daily ET flux | W m-2 day-1 |
| HDAY.bin | Daily H flux | W m-2 day-1 |
| GDAY.bin | Daily G flux | W m-2 day-1 |
| SDDAY.bin | Daily SD flux | W m-2 day-1 |
| SNETDAY.bin | Daily SNET flux | W m-2 day-1 |
| LWDNDAY.bin | Daily LW down flux | W m-2 day-1 |
| LWUPDAY.bin | Daily LW up flux | W m-2 day-1 |
| ESI_2week.bin | 2 weeks composite ESI | % |
| ESI_4week.bin | 4 weeks composite ESI | % |
| ESI_8week.bin | 8 weeks composite ESI | % |
| ESI_12week.bin | 12 weeks composite ESI | % |

The QC of the daily fluxes (QC shortwave downward surface radiative flux) contains flag values indicating various quality conditions of the fluxes.  The flags are packed bitwise according to the following table.

## 3.2 GRIB Edition 2 (GRIB2) messages

GET-D HDF data files contain one science data set for all of the 11 output variables and their qc information.  The data are stored in original float format without any scaling. GRIB2 data filenames are of the form:

GETD_GRIB2_yyyyddd.grb2

YYYY = current Year

ddd    = current Julian day

## 3.3 Network Common Data Format (netCDF) Data

GET-D netCDF data files contain the latitude, longitude, and all of the 11 output variables and their qc information.  The parameters (except unscaled pixel coordinates) are stored scaled, short integers or scaled byte values, in order to reduce file volume.  The scaled short integers and scaled byte values must be unscaled and restored to real (float) data values. Metadata are in the NETCDF file to give scaling factors for restoring the integer or byte values back into real values.

Each hyperslab contains a 2-dimensional array of numbers.

NetCDF data filenames are of the form:

GETD_NETCDF_YYYYddd.nc

where          YYYY = current Year

ddd    = current Julian day

## 3.4 Portable Network Graphics (PNG) Image Files

The GET-D system generates images for web publishing and/or internal monitoring. Images are produced for GET-D composite Evaporative Stress Index (ESI) only.

The PNG image filenames are of the form:

YYYYMMDD_<parameter>Week.png

Where YYYY = 4 digits year

DD	= 2 digits day of the year

<parameter>	= GET-D composite week numbers, 02, 04, 08 and 12

Example: on

20151001_02Week.png

20151001_04Week.png

20151001_08Week.png

20151001_12Week.png

# 4.0 ANCILLARY FILES

The GET-D ancillary files contain static data needed by the algorithms during GET-D processing, such as algorithm coefficients, land surface classes, and climatology data.  They are “static” because they do not change temporally (but may be updated from time to time). Ancillary files are either in ASCII format or binary format.

All GET-D ancillary files are found in the system’s static directory (default is data/static).

## 4.1 Static files used for CFS processing

Table 4.1 Static files used for CFS processing.

| Directory | File name | Notes |
| --- | --- | --- |
| $HOME/data/static | CFS_landcover_2012.dat | Land cover of CFS data |
| $HOME/data/static | landmask_UMD.1gd4r | UMD land mask data |
| $HOME/data/static | region_lc.dat | Land cover mask for the NA domain |

## 4.2 Static files used for GOES data processing

Table 4.2 Static files used for GOES processing.

| Directory | File name | Notes |
| --- | --- | --- |
| $HOME/data/static | landmask_goes_east_v2.dat | Land mask of GOES EAST data |
| $HOME/data/static | landmask_goes_west_v2.dat | Land mask of GOES WEST data |
| $HOME/data/static | landmask_UMD.1gd4r | UMD land mask data |
| $HOME/data/static | view_angle.dat | GOES view angle |
| $HOME/data/static/EAST_MASK/ | CHAN_DIFF_NEG_DIFF_SMOOTH MAX_TB11_SMOOTH VIS_ALBEDO_SMTH CHAN_DIFF_POS_DIFF_SMOOTH SUNRISE | Climatology data used for GOES EAST cloud masking |
| $HOME/data/static/WEST_MASK/ | CHAN_DIFF_NEG_DIFF_SMOOTH MAX_TB11_SMOOTH VIS_ALBEDO_SMTH CHAN_DIFF_POS_DIFF_SMOOTH SUNRISE | Climatology data used for GOES WEST cloud masking |

## 4.3 Static files used for GSIP processing

Table 4.3 Static files used for GSIP processing.

| Directory | File name | Notes |
| --- | --- | --- |
| $HOME/data/static | na8km_dummy.dat | Dummy file used to replace the missing hourly insolation data. |
| $HOME/data/static | landmask_UMD.1gd4r | UMD land mask data |

## 4.4 Static files used for VIIRS processing

Table 4.4 Static files used for VIIRS data processing.

| Directory | File name | Notes |
| --- | --- | --- |
| $HOME/data/static | VIIRS_global_GVF_climatology.h5 | Climatology data used for VIIRS GVF. |
| $HOME/data/static | EVI_b0.dat | Parameter used for linear regression |
| $HOME/data/static | EVI_b1.dat | Parameter used for linear regression |

## 4.5 Static files used for snow mask processing

Table 4.5 Static files used for snow mask data processing.

| Directory | File name | Notes |
| --- | --- | --- |
| $HOME/data/static | imslon_24km.dat | Lon index file used to remap the snow mask |
| $HOME/data/static | imslat_24km.dat | Lat index file used to remap the snow mask |
| $HOME/data/static | landmask_UMD.1gd4r | UMD land mask data |

## 4.6 Static files used for ET/ESI processing

Table 4.6 Static files used for ET/ESI data processing.

| Directory | File name | Notes |
| --- | --- | --- |
| $HOME/data/static | region_adeadl.dat region_adeadn.dat region_adeadv.dat region_aleafl.dat region_aleafn.dat region_aleafv.dat region_xl.dat | Surface parameters in NA domain. |
| $HOME/data/static | FINAL_RS_CORR_NAMR_WARM_T5T21.dat | Soil reflectance |
| $HOME/data/static | landmask_UMD.1gd4r | UMD land mask data |
| $HOME/data/static/inso | alexi_insol15_smth_2011[ddd].dat alexi_insol55_smth_2011[ddd].dat | Climatology insolation data ddd – day of the year, range from 001 to 365 |

# Reference