## Slide 1: GOES Evapotranspiration and Drought Product System (GET-D) Operational Readiness Review (ORR) February 3, 2016
Prepared By: Hanjun Ding (OSPO), Jerry Zhan (STAR), Rao Venkata(SGT) Zhengping Li (IMSG), Priyanka Roy (IMSG)

## Slide 2: ORR Agenda
Introduction Ding
Risks and Actions Ding
System Requirements Roy
System Description Venkata
System Test Venkata
System Operational Readiness Ding
Summary Ding

## Slide 3
Section 1 –
Introduction
Hanjun Ding

## Slide 4: Project Objectives
ET and drought maps generated from the Atmosphere-Land Exchange Inversion model (ALEXI) for NCEP/NIDIS/USDA users
The products are generated from the brightness temperature (BT) of the GOES East and West Imagers
Coverage and resolution: North America at a spatial resolution of 8 km
ET product: Daily, over clear-sky pixels
Drought product: 2, 4, 8, 12-week composites updated daily
Output format: GRIB2, NetCDF and PNG

## Slide 5: Integrated Product Team
IPT Lead: Xiwu (Jerry) Zhan (STAR)
IPT Backup Lead: Hanjun Ding (OSPO)
NESDIS Team:
  STAR: Chris Hain, Li Fang, Zhengpeng Li , Priyanka Roy, Istvan Laszlo
  OSPO: Hanjun Ding, Zhaohui Cheng, Ricky Irving
  OSD: Tom Schott
  Data Center: Phil Jones (NCDC)
  Others: Venkata Rao Anne (SGT)
User Team
  Lead: Mike Ek (NCEP-EMC)
  Others:
    NCEP-EMC: Youlong Xia
    NCEP-CPC: Kingtze Mo, Jin Huang
    NDMC-UNL: Brian Wardlow, Mark Svoboda
    USDA: Martha Anderson (ARS), Zhengwei Yang (NASS), Curt Reynolds (FAS)
Oversight Panel (OP) lead: Land POP
Other OPs involved: ERBPOP

## Slide 6: Project Stakeholders
NESDIS
  STAR
  OSPO
  OSGS
  NCEI
  NDE
NWS/NCEP EMC
NWS/NCEP CPC
NDMC-UNL
USDA FAS

## Slide 7: Project Plan (1)
Year 1 – Design and Development (2013 – 2014)
  Develop Requirements Document
  Identify ancillary data for the algorithms
  Conduct CDR
  Compute software development

## Slide 8: Project Plan (2)
Year 2 –Transition to Pre-Operations (2014 – 2015)
  Deliver initial DAP (Framework with pre-operational algorithms) to OSPO
  Conduct Software Review
  Update algorithms
  Transition and test system within the OSPO environment
  Perform test data flows
  Conduct System Readiness Review
  Deliver final DAP to OSPO
Notes: Priyanka: Changed “Test Readiness Review” to “Algorithm Readiness Review”
Priyanka: Deleted slide Project Plan (3)

## Slide 9
Project Timeline
ORR 02/03/16
Notes: Priyanka 09/03/14: Updated

## Slide 10: Project Milestones
Critical Design Review – 08/21/2014
Software Review – 7/17/2015 (October 2014)
System Readiness Review – 08/31/2015 (October 2014)
Operational Readiness Review – 02/03/2016 (September 2015)
SPSRB Briefing – 02/17/2016

## Slide 11: ORR Entry Criteria
Requirements Document
  SPSRB #0905-0007, “A GOES Thermal Observation Based Evapotranspiration (ET) Product”
Review Contents:
  Requirements
  Software Architecture
  Algorithm Readiness
  Risks and Actions

## Slide 12: ORR Exit Criteria
GET-D ORR Report
  The report will contain:
    Actions
    Comments
    ARR presentation
Updated GET-D Review Item Disposition (RID) spreadsheet.
Updated GET-D Requirements Allocation Document (RAD)

## Slide 13
Introduction
Risks and Actions
System Requirements
System Description
System Test
System Operational Readiness
Summary
13
Outline
Notes: 13
Priyanka: Changed
--“Project Plan” to “Introduction”
--“PDR Report to PDR Risks and Actions”

## Slide 14
Section 2
Pre-ORR Risks and Actions
Hanjun Ding

## Slide 15: CDR Risks and Actions
Risk # 1: Unavailability of optimal EVI data for input to the model that will eventually be used for creating the ESI climatology. Presently EVI is calculated from MODIS LAI product.
Impact: If a optimal EVI is not available, the quality of the drought product will be degraded.
Mitigation: A regression approach is being explored to estimate LAI from either:
  VIIRS EVI
  surface reflectance
Likelihood: Low
Severity: High
Assessment: Medium
Status: Closed
1
2
3
4
5
5
4
3
2
1
CONSEQUENCES
LIKELIHOOD
X

## Slide 16: CDR Risks and Actions
Risk # 2: Project schedule will be impacted if the FY14 hardware purchase delay continues, since OSPO process for procuring hardware has changed with the new O&M contract.
Impact: Project Schedule.
Mitigation:
Likelihood: Medium
Severity: Medium
Assessment: Medium
Status: Closed
1
2
3
4
5
5
4
3
2
1
CONSEQUENCES
LIKELIHOOD
X

## Slide 17: CDR Risks and Actions
Risk # 3: If the VIIRS Geolocation file (GITCO) is not included as an input to the GET-D System, the VIIRS VI EDR files will not be geolocated.
Impact: Product Quality.
Mitigation: Included GITCO file in the input
Likelihood: Low
Severity: High
Assessment: Medium
Status: Closed
1
2
3
4
5
5
4
3
2
1
CONSEQUENCES
LIKELIHOOD
X

## Slide 18: CDR Risks and Actions
Risk # 4: If the plan to archive the product is not finalized, this product will not be archived.
Impact: Data archive.
Mitigation: The data submission agreement has already been submitted. Will follow up with NCDC and work with Phil Jones to finalize the process.
Likelihood: Medium
Severity: High
Assessment: High
Status: Open
1
2
3
4
5
5
4
3
2
1
CONSEQUENCES
LIKELIHOOD
X

## Slide 19: CDR Risks and Actions
Risk # 5: Following OSPO's SMOMS contract situation, the project schedule may be impacted due to lack of SMOMS contract support.
Impact: Product Schedule.
Mitigation: PAL will work to ensure contract support is available.
Likelihood: Medium
Severity: High
Assessment: High
Status: Closed
1
2
3
4
5
5
4
3
2
1
CONSEQUENCES
LIKELIHOOD
X

## Slide 20: CDR Risks and Actions
Risk # 6: There might be delay in testing if OSPO is not able to allot required disk storage for testing.
Impact: Product schedule.
Mitigation: STAR developers will provide am estimate of disk storage required for testing to OSPO.
Likelihood: Low
Severity: High
Assessment: Medium
Status: Closed
1
2
3
4
5
5
4
3
2
1
CONSEQUENCES
LIKELIHOOD
X

## Slide 21: CDR Risks and Actions Summary
There were 6 CDR Risks and 5 are recommended to be closed
Open Risks Assessment: 1 High

## Slide 22: ARR Risks and Actions
Review 1: Provide output file location and distribution information to user at least 1 week before data is sent out to allow time for making changes in scripts on the user side.
Mitigation: PAL will work with CPC user and OSPO’s product distribution team to provide the necessary information
Status: Closed

## Slide 23: Risks and Actions Summary
Summary of Risks and Actions after ORR
  1 CDR risk remain open
  Open Risks Assessment: 1 High
Notes: 23

## Slide 24
Introduction
Risks and Actions
System Requirements
System Description
System Test
System Operational Readiness
Summary
24
Outline
Notes: 24
Priyanka: Changed
--“Project Plan” to “Introduction”
--“PDR Report to PDR Risks and Actions”

## Slide 25
Section 3 –
Requirements
Jerry Zhan Felix Kogan

## Slide 26: Requirements Overview
All GET-D Project requirements are presented in this section.
All GET-D Project requirements are documented in a single RAD located in the project repository at:
Basic requirements are shown in all yellow text on a single slide.
Requirements which have been updated/added since the last review are in green.
Notes: Changed, document name: “Joint Polar Satellite System (JPSS) Program Level 1 Requirements SUPPLEMENT – Final”

## Slide 27: Basic Requirement 0
GET_D-R 0: The GOES Evapotranspiration and Drought (GET-D) Product System shall adopt the standard practices of the SPSRB Review Process
  Driver: SPSRB transition to operations process

## Slide 28: Basic Requirement 0.0
GET_D-R 0.1: The GET-D SPSRB reviews shall be tailored
  This derived requirement has been adopted to mitigate schedule risk by eliminating the overhead of preparing review slide packages and reports. Details are in derived requirements 0.1.x.

## Slide 29: Basic Requirement 0.0
GET_D-R 0.1.1: There shall be a Critical Design Review (CDR) (that contains information from a Requirements Review and the Preliminary Design Review) for GET-D.
  This derived requirement has been adopted to mitigate schedule risk by eliminating the overhead of preparing a Requirements Review, PDR, and CDR slide packages separately. The Technical risk is assessed as Low because the CDR will be tailored to accomplish the standard objectives of a PDR and Requirements Review. Risks shall be tracked.

## Slide 30: Basic Requirement 0.0
GET_D-R 0.1.2: The Critical Design Review Report (CDRR), a standard artifact of the SPSRB Process shall be compiled for the GET-D project.
  The CDRR is one of the exit criteria for the CDR. The updated CDR slides will form the CDRR.
GET_D-R 0.1.3: There shall be a Software Code Review (SCR) for GET-D.
  This derived requirement has been adopted for meeting OSPO coding and security standards.

## Slide 31: Basic Requirement 0.0
GET_D-R 0.1.4: There shall be an System Readiness Review (SRR) for GET-D.
  This derived requirement has been adopted from the SPSRB review process.
GET_D-R 0.1.5: The System Readiness Review Report (SRRR), a standard artifact of the SPSRB Process shall be compiled for the GET-D project.
  The SRRR is an exit criteria for the SRR.

## Slide 32: Basic Requirement 0.0
GET_D_R 0.1.6: There shall be an Operational Readiness Review (ORR) for GET-D.
  This derived requirement has been adopted from the SPSRB review process.
GET_D_R 0.1.7: The Operational Readiness Review Report (ORRR), a standard artifact of the SPSRB Process shall be compiled for the GET-D project.
  The ORRR is an exit criteria for the ORR.

## Slide 33: Basic Requirement 0.0
GET_D-R 0.2: The Requirements Allocation Document (RAD) shall be created and maintained by the GET-D development team.
  This derived requirement has been adopted from the SPSRB Review process. The RAD will follow document standards stated in EPL v3 process asset DG-6.2
GET_D-R 0.3: The Review Item Disposition (RID) spreadsheet shall be created and maintained by the GET-D development team.
  This derived requirement has been adopted from the SPSRB Review process.

## Slide 34: Basic Requirement 0.0
GET_D-R 0.4: Configuration Management shall be implemented for the GET-D software and documentation.
  Project documents will be distributed through Google Drive. Code and test data will be distributed via ftp transfer.

## Slide 35: Basic Requirement 1
GET_D-R 1: The GET-D system shall generate GOES Thermal observation based evapotranspiration (ET) and drought monitoring products.
  Driver: This basic requirement is traced to user needs as stated in the SPSRB User request # 0905-0007, A GOES Thermal Observation Based Evapotranspiration (ET) Product: NCEP needs independent ET data from satellite for validating Noah land surface model output and satellite based drought data product for monthly drought briefing

## Slide 36: Basic Requirement 1.0
GET_D-R 1.1: The GET-D evapotranspiration product shall be generated daily over clear sky conditions.
  User Request.
GET_D-R 1.2: The GET-D drought product shall be generated as 2, 4, 8, 12 weeks composite drought maps updated daily.
  Standard format for this user community.

## Slide 37: Basic Requirement 1.0
GET_D-R 1.3: The GET-D output file shall include daily sensible heat flux (H), soil heat (G), net radiation Rn and its components (upward and downward longwave radiation fluxes and solar insolation).
  Provided for users' convenience.
GET_D-R 1.4: The GET-D products shall have a full coverage of the North America region.
  User Request. Current capabilities

## Slide 38: Basic Requirement 1.0
GET_D-R 1.5: The GET-D product shall be a land surface product with a horizontal resolution of 10 km.
  User Request. Current capabilities
GET_D-R 1.6: The GET-D products shall be in Lat/Lon projection.
  User Request.

## Slide 39: Basic Requirement 1.0
GET_D-R 1.7: The GET-D products shall have error less than 20%.
  User Request.
GET_D-R 1.8: The GET-D products shall have a latency in the range 3 to 6 hours.
  User Request.
GET_D-R 1.9: The GET-D products shall include quality information.
  QC flags will be specified in the External Users Manual.

## Slide 40: Basic Requirement 1.0
GET_D-R 1.10: The GET-D system shall write the Evapotranspiration and Drought Monitoring products into a single file written in NetCDF4
  The NetCDF4 output will be for the archives.
GET_D-R 1.11: The GET-D system shall produce Evapotranspiration and Drought monitoring tailored products in GRIB2 and PNG formats.
  User Request.

## Slide 41: Basic Requirement 1.0
GET_D-R 1.12: The GET-D developers shall perform validation and verification of the GET-D products.
GET_D-R 1.12.1: The GET-D developers shall perform unit testing to verify functional performance of the code that produces the GET-D products.
  Will be included in the unit tests and the system test described in the SRR.

## Slide 42: Basic Requirement 1.0
GET_D-R 1.12.2: The GET-D developers shall verify the error handling capability of the pre-operational system.
  Needed by OSPO for reliable operations.
GET_D-R 1.12.3: The GET-D developers shall produce and distribute the ET and Drought monitoring product files for evaluation by the user community.
  Standard procedure for this user community.

## Slide 43: Basic Requirement 1.0
GET_D-R 1.12.4: The GET-D system shall perform routine data range checks to flag anomalous values in the input data.
  Anomalous values will be flagged. These checks will be included in the code and described in the SRR.
GET_D-R 1.12.5: The GET-D system shall perform routine data range checks to flag anomalous values in the ET and Drought Products.
  Out-of-range values will be flagged. These checks will be included in the code.

## Slide 44: Basic Requirement 2
GET_D-R 2: The GET-D system shall have data ingest capability.
  Driver: This basic requirement is traced to algorithm input needs as documented in the GET-D ATBD.

## Slide 45: Basic Requirement 2.0
GET_D-R 2.1: The GET-D system shall ingest GOES Brightness Temperature and solar insolation.
GET_D-R 2.2: The GET-D system shall ingest VIIRS EVI generated by IDPS.
Notes: Priyanka 09/03/14: Updated

## Slide 46: Basic Requirement 2.0
GET_D-R 2.3: The GET-D system shall ingest NOAA IMS Snow mask.
GET_D-R 2.4: The GET-D system shall ingest GFS meteorological fields.
GET_D-R 2.5: The GET-D system shall ingest VIIRS Geolocation file (GITCO).

## Slide 47: Basic Requirement 3
GET_D-R 3: The GET-D system shall implement the ALEXI algorithm to generate the ET and drought monitoring products.
  Driver: This basic requirement is traced to user needs for the GET-D products.

## Slide 48: Basic Requirement 3.0
GET_D-R 3.1: The GET-D algorithms shall be implemented by processing codes written in Fortran 95.
GET_D-R 3.2: The GET-D processing code shall be able to run in the Development Environment at STAR.
  Fortran code can run in this environment

## Slide 49: Basic Requirement 3.0
GET_D-R 3.3: The GET-D processing code shall be able to run in the OSPO Test Environment.
  Fortran code can run in this environment
GET_D-R 3.4: The GET-D processing code shall be able to run in the OSPO Operational Environment.
  Fortran code can run in this environment
GET_D-R 3.5: The GET-D algorithm shall generate QC flags.

## Slide 50: Basic Requirement 4
GET_D-R 4: The GET-D system shall generate metadata for retrieved product.
  Driver: This basic requirement is traced to OSPO needs for monitoring and maintenance.

## Slide 51: Basic Requirement 4.0
GET_D-R 4.1: The GET-D system shall write metadata text files associated with the retrieved products.
GET_D-R 4.2: The metadata shall include overall quality and summary level metadata.
GET_D-R 4.3: The metadata shall include Granule metadata.

## Slide 52: Basic Requirement 5
GET_D-R 5: The GET-D system shall have QC monitoring capability
  Driver: This basic requirement is traced to an OSPO need for QC monitoring.

## Slide 53: Basic Requirement 5.0
GET_D-R 5.1: The GET-D system output shall include overall quality control flags and quality summary level metadata
  Needed for distribution, archive, quality control and post-processing in the products files. GET-D code will generate metadata for this purpose.

## Slide 54: Basic Requirement 5.0
GET_D-R 5.2: The GET-D system shall be capable of monitoring input data latency and overall quality
GET_D-R 5.3: The GET-D system shall be capable of monitoring product latency
  Output GET-D processing time and output to status file

## Slide 55: Basic Requirement 5.0
GET_D-R 5.4: The GET-D system shall produce real-time PNG imagery files for visual inspection of output data files
  PNG files will be produced by the Product Output Processor Unit
GET_D-R 5.5: The GET-D system shall be capable of monitoring product distribution status to ensure that the data/products are successfully available for transfer to the user community
  A product status file will be produced for each operational run

## Slide 56: Basic Requirement 5.0
GET_D-R 5.6: The GET-D system shall generate log files for every run.
  Needed to ensure the run was completed successfully.

## Slide 57: Basic Requirement 5.0
GET_D-R 5.6.1: Each log file shall include all runtime error messages
  Error messages will include system messages and error conditions written by the code
GET_D-R 5.6.2: The log file shall indicate whether or not the run was completed without error
  Code will write this message. This indication will be the last message in the file, so that operators can find it easily

## Slide 58: Basic Requirement 6
GET_D-R 6: The GET-D developers shall produce a fully functional pre-operational system in the STAR Development Environment
  Driver: This basic requirement is traced to an OSPO need for a fully functional system ready for integration and system testing

## Slide 59: Basic Requirement 6.0
GET_D-R 6.1: The Development Environment shall host the pre-operational system
  Pre-operational system is to be developed in this environment
GET_D-R 6.1.1: The Development Environment shall include C, gcc, and gfortran compilers
  Needed for the code

## Slide 60: Basic Requirement 6.0
GET_D-R 6.1.2: The Development Environment shall have 4 GB of memory
  Memory capacity requirement is based on experience with the GET-D R&D code
GET_D-R 6.1.3: The Development Environment shall have 1 TB of data storage
  Data storage capacity requirement is based on experience with the GET-D R&D code

## Slide 61: Basic Requirement 6.0
GET_D-R 6.1.4: The Development Environment shall include C, MATLAB, and HDF 4.2 libraries
  Needed for running the code
GET_D-R 6.1.5: The Development Environment shall include Perl, IDL, bash shell, and C shell
  Needed for running the code

## Slide 62: Basic Requirement 6.0
GET_D-R 6.2: The Development Environment shall be capable of hosting unit tests
GET_D-R 6.2.1: The Development Environment shall have a link to SATEPSANONE server
  Needed for ingest of GSIP data.

## Slide 63: Basic Requirement 6.0
GET_D-R 6.2.3: The pre-operational system shall include all processing code and ancillary files needed to conduct unit tests
  Complete unit test of each stage of the pre-operational system is expected before delivery to OSPO
GET_D-R 6.2.4: The pre-operational system shall include all input test data needed to conduct unit tests
  Complete unit test of each stage of the pre-operational system is expected before delivery to OSPO

## Slide 64: Basic Requirement 7
GET_D-R 7: The GET-D pre-operational system shall be transitioned from the STAR Development Environment to the OSPO Test Environment
  Driver: This basic requirement is traced to an OSPO need for a fully functional system in its Test Environment.

## Slide 65: Basic Requirement 7.0
GET_D-R 7.1: The pre-operational system shall include all processing code and ancillary files needed to reproduce the unit tests
  For system testing. A complete system test of the integrated pre-operational system is expected before delivery to OSPO Test Environment

## Slide 66: Basic Requirement 7.0
GET_D-R 7.2: The pre-operational system shall include all input test data needed to reproduce the unit tests
  Complete system test of the pre-operational system is expected
GET_D-R 7.3: The pre-operational system shall include all intermediate files produced by the unit tests
  Complete system test of the pre-operational system is expected

## Slide 67: Basic Requirement 7.0
GET_D-R 7.4: The integrated pre-operational system shall include all output data produced by the unit tests
  Needed by OSPO to verify the system tests in its Test Environment

## Slide 68: Basic Requirement 7.0
GET_D-R 7.5: The GET-D development team shall set up an internal FTP site for transferring the pre-operational system to OSPO as a tar file on a STAR server that is accessible to OSPO
GET_D-R 7.5.1: The GET-D development team shall ensure that the OSPO PAL has the information needed to acquire the pre-operational system as a tar file

## Slide 69: Basic Requirement 8
GET_D-R 8: The GET-D developers shall specify IT resource needs for operations
  Driver: OSPO IT Capacity Planning

## Slide 70: Basic Requirement 8.0
GET_D-R 8.1: The GET-D system shall be able to process data using 1 TB of data storage
GET_D-R 8.2: The GET-D system shall be able to process data using 4 GB of RAM
GET_D-R 8.3: The GET-D system shall be able to operate on VMWare Linux

## Slide 71: Basic Requirement 8.0
GET_D-R 8.4: The GET-D system shall be able to process using C, gcc, g95 and gfortran compilers
  Needed for the code
GET_D-R 8.5: The GET-D system shall be able to process using C, MATLAB, and HDF 4.2 libraries
  Needed for running the code

## Slide 72: Basic Requirement 8.0
GET_D-R 8.6: The GET-D system shall be able to process using Perl, IDL, bash shell, and C shell
  Needed for running the code
GET_D-R 8.7: The GET-D system shall be able to process using GRADS
  Needed for postprocessing

## Slide 73: Basic Requirement 9
GET_D-R 9: The GET-D pre-operational system shall be delivered to OSPO for integration into their operational system as a Delivered Algorithm Package (DAP).

## Slide 74: Basic Requirement 9.0
GET_D-R 9.1: The DAP shall contain science algorithm source code, including make files and scripts.
GET_D-R 9.2: The DAP shall contain test plans, test description, test procedures, and detailed performance testing results.

## Slide 75: Basic Requirement 9.0
GET_D-R 9.3: The DAP shall contain test input data, temporary files, and expected output data.
GET_D-R 9.4: The DAP shall contain coefficient files and/or look-up tables.
GET_D-R 9.5: The DAP shall contain quality monitoring information (quality flags, quality flag values).

## Slide 76: Basic Requirement 9.0
GET_D_R 9.6: The DAP shall contain product file specifications -- layout, content, and size.
GET_D_R 9.7: The DAP shall contain data flow diagrams.
GET_D_R 9.8: The DAP shall contain list of exit codes and their associated messages.
Notes: Priyanka 09/03/14: Updated

## Slide 77: Basic Requirement 9.0
GET_D-R 9.9: The DAP shall contain list of expected compiler warnings.
GET_D-R 9.10: The DAP shall contain estimates of resources required for execution.
GET_D-R 9.11: The DAP shall contain Algorithm Theoretical Basis Documents (ATBDs) or reference to where the ATBDs can be obtained.

## Slide 78: Basic Requirement 9.0
GET_D-R 9.12: The DAP shall contain Delivery Memo.
GET_D-R 9.12.1: The delivery memo shall include the point(s) of contact for questions specific to the algorithm (include name, telephone, and e-mail address). At a minimum, include algorithm developer and PAL.

## Slide 79: Basic Requirement 9.0
GET_D-R 9.12.2: The delivery memo shall include the list of delivery contents.
GET_D-R 9.12.3: The delivery memo shall include the purpose of the delivery (e.g. an initial release, modification).
GET_D-R 9.12.4: The delivery memo shall include the description of significant changed from previous version, if any.

## Slide 80: Basic Requirement 9.0
GET_D-R 9.12.5: The delivery memo shall include the description of problem(s) resolved, if any, and method of resolution.
GET_D-R 9.12.6: The delivery memo shall include the list of documents updated/added/superseded, if any.
GET_D-R 9.12.7: The delivery memo shall include the list of known remaining defects.

## Slide 81: Basic Requirement 9.0
GET_D-R 9.13: The DAP shall contain README text file.
GET_D-R 9.13.1: The README text shall include the DAP version number.
GET_D-R 9.13.2: The README text shall include the location of all required DAP contents.

## Slide 82: Basic Requirement 9.0
GET_D-R 9.13.3: The README text shall include the target configuration for setup (directories and files after setup scripts have been executed). This is understood to be a list of where everything is located once the DAP has been unpacked.
GET_D-R 9.13.4: The README text shall include the other pertinent information as judged by the algorithm developer(s) (compiler settings, etc.)

## Slide 83: Basic Requirement 10
GET_D-R 10: STAR shall deliver GET-D SPSRB documents to OSPO
  Driver: This basic requirement is traced to an OSPO need for documentation to support operations, maintenance, and distribution

## Slide 84: Basic Requirement 10.0
GET_D-R 10.1: The GET-D document package shall include an Algorithm Theoretical Basis Document (ATBD).
  The ATBD will follow SPSRB Version 2 document standards

## Slide 85: Basic Requirement 10.0
GET_D-R 10.2: The GET-D document package shall include a System Maintenance Manual (SMM).
  The SMM will follow SPSRB Version 2 document standards
GET_D-R 10.3: The GET-D document package shall include a External Users Manual (EUM).
  The EUM will follow SPSRB Version 2 document standards

## Slide 86: Basic Requirement 11
GET_D-R 11: The GET-D system shall comply with OSPO Code Review Security check lists
  Driver: OSPO code standards and OSPO security requirements

## Slide 87: Basic Requirement 11.0
GET_D-R 11.1: The GET-D system shall comply with OSPO data integrity check list.
GET_D-R 11.2: The GET-D system shall comply with OSPO development security check list
  OSPO development security check list is part of the OSPO Code Review Security check lists
GET_D-R 11.3:The GET-D system shall comply with OSPO code check list.
  OSPO code check list is part of the OSPO Code Review Security check lists

## Slide 88: GET-D System Requirements – Summary
The GET-D System Requirements have been established.
The Requirements have been documented in the Requirements Allocation Document (RAD).
The Requirements are traceable to drivers (customer needs or expectations) and other requirements.
Updated requirement has been reviewed.

## Slide 89
Introduction
Risks and Actions
System Requirements
System Description
System Test
System Operational Readiness
Summary
89
Outline
Notes: 89
Priyanka: Changed
--“Project Plan” to “Introduction”
--“PDR Report to PDR Risks and Actions”

## Slide 90
Section 4 –
System Description
Rao Venkata

## Slide 91: Operations Concept
  What is the product?
  Why is this product being produced?
  How should this product be produced (operational scenario)?
The operations concept refined by the Integrated Product Team (IPT) of GOES Evapotranspiration (ET) and Drought (GET-D) Product system, in consultation with customers/users, as the product solution and design are matured through the design development phase.

## Slide 92: What is the Product?
The GET-D system produce a daily product that consists of two drought indices:
  Evapotranspiration (ET)
  Evaporative Stress Index (ESI)
Each index will be a North America gridded composite map in Lat/Lon projection with 10 km resolution at the equator.

## Slide 93: Why Are The Products Being Produced?
NCEP needs independent ET data from satellite for validating Noah land surface model output and satellite based drought data product for monthly drought briefing
USDA ARS is contributing the drought monitoring product based on the Evaporative Stress Index (ESI) to the National Integrated Drought Information System (NIDIS), which requires an operational production system to generate composited ESI based on NOAA GOES satellite observations
The independent information of the ET and ESI based on GOES satellite observations is useful to the US and Work Crop forecasts that are mandates of USDA-NASS and USDA-FAS respectively.

## Slide 94: How Should The Products Be Produced?
There will be three distinct environments
  Development Environment (STAR)
    Development and unit testing of pre-operational codes conducted on Redhat Linux OS in STAR
  Test Environment (OSPO)
    Pre-operational codes and documents (DAP) received from STAR implemented and tested on Linux machine (GSRDEV) and modified as needed before it is promoted to operations
  Operations Environment (OSPO)
    Operational DAP will be run on Linux machine (GSRPROD) and the products monitoring GUI will be posted on the intranet web server and accessed under ESPC VPN by operators, PALs and maintenance programmers

## Slide 95: GET-D System Design
The GET-D system provides an infrastructure that will enable the implementation of the GET-D algorithms to meet requirements.

## Slide 96: GET-D IT System Architecture

## Slide 97: System Test Environment
The System tests are performed on gsrdev.espc.nesdis.noaa.gov – Red Hat Enterprise Linux Server 6.6).
This machine is located at NSOF and is maintained by OSPO IT.
  6 CPUs
  2.0 GHz
  16 GB memory
  2 TB disk space
  GFORTRAN
The NetCDF, HDF4 and GRIB2 libraries are the stable versions:
  netcdf-4.2-gfortran(GFortran77/90/95)
  HDF5
  GRIB2 1.4.0

## Slide 98: GET-D Major Components
Meteorological Forcing Processor (MFP)
  Type: Processing Unit
  Description: Pre-Processor meteorological forcing datasets
Satellite Dataset Processor (SDP)
  Type: Processing Unit
  Description: Pre-Processor satellite datasets, including GOES BT, solar insolation from GSIP products, Vegetation index maps, real-time cloud mask and snow mask
Ancillary Dataset Processor (ADP)
  Type: Processing Unit
  Description: Pre-Processor ancillary datasets, including land cover map and satellite viewing geometry

## Slide 99: GET-D Major Components
ALEXI core processor (ALEXI)
  Type: Processing Unit
  Description: Calculate daily ET and potential ET from inputs.
Quality Control Flags (QCF)
  Type: Processing Unit
  Description: Generate quality control flags for each pixel
Product Output Processor (POP)
  Type: Processing Unit
  Description: Output ET and drought products in required data formats (NetCDF, GRIB2 and PNG)

## Slide 100: GET-D Context Layer Data Flow
Data processing unit
External inputs
Software system
ALEXI model
Daily ET product with QC
ESI product with QC
External outputs
Satellite-based observations
Meteoro-logical data
Ancillary data
Daily radiance and fluxes
With QC

## Slide 101: GET-D Data Flow

## Slide 102: GET-D System Level - Input
Name | Category | Source | Description
Brightness temperature | Satellite observation | GOES | GOES East/West Imagery; 11micron/3.9 micron brightness temperature
Insolation | Satellite observation | GSIP | GSIP real time insolation
Vegetation Index | Satellite observation | VIIRS | VIIRS EVI
Snow mask | Satellite observation | NOAA IMS | IMS Daily Northern Hemisphere Snow and Ice Analysis
Air temperature | Meteorological data | CFS | Surface and pressure level profiles
Specific humidity | Meteorological data | CFS | Surface and pressure level profiles
Geopotential height | Meteorological data | CFS | Surface and pressure level profiles
Wind speed | Meteorological data | CFS | Surface
Downwelling longwave radiation | Meteorological data | CFS | Surface
Land Cover | Ancillary data | University of Maryland | Land cover classes in 1km resolution (static)
Albedo | Ancillary data | MODIS | Surface Albedo from MODIS (static)
Clear day insolation | Ancillary data | GSIP | Clear day insolation (static)

## Slide 103: GET-D System Level - Outputs
Variables | Source | Spatial Domain | Spatial resolution | Description
ET product with QC | GET-D | North America | 8 km | Daily ET map
ESI products with QC | GET-D | North America | 8 km | 2,4,8, 12-week composite drought map
Flux products with QC | GET-D | North America | 8 km | Daily sensible heat and soil heat flux map
Radiance products with QC | GET-D | North America | 8 km | Daily short wave down, long wave down, long wave up and net radiation map

## Slide 104: System Description Production
GETD generates one set of gridded data product over the North America domain per day:
  Daily ET
  2, 4, 8, 12-week ESI
  Daily radiances and fluxes
Each product contains ET, ESI and other data layers with the QC flags for each grid.
Each product has file size of approximately 30 MB in raw binary data.

## Slide 105: System Description Production - GRIB2
Layer | Data description | Number (In Section 4, octet 11) | Unit | Data type | Fill value | Valid range | Scale factor
1 | Daily ET | 6 | MJ m-2 day-1 | real | -9999 | 0 - 1000 | 1
2 | Daily ET QC | 231 | N/A | 1-byte integer | 256 | N/A | N/A
3 | 2, 4, 8, 12 -week ESI | 232, 234, 236, 238 | N/A | real | -9999 | -5 – 5 | 1
4 | 2, 4, 8, 12 -week ESI QC | 233, 235, 237, 239 | N/A | 1-byte integer | 256 | N/A | N/A
5 | SD, SNET, LWDN, LWUP | 240, 242, 244, 246 | MJ m-2 day-1 | real | -9999 | 0 – 1000 | 1
6 | SD, SNET, LWDN, LWUP QC | 241, 243, 245, 247 | N/A | 1-byte integer | 256 | N/A | N/A
7 | H, G | 248, 250 | MJ m-2 day-1 | real | -9999 | - 1000 – 1000 | 1
8 | H, G QC | 249, 251 | N/A | 1-byte integer | 256 | N/A | N/A

## Slide 106: System Description Production – NetCDF4
Global attributes:
  title = "GETD product"
  Date = “2013-08-01”
Variables:
  float Longitude(Longitude) ;
  Longitude:units = "degrees_east" ;
  float Latitude(Latitude) ;
  Latitude:units = "degrees_north" ;
  int ET(Latitude, Longitude) ;
  ET:units = “MJ m-2 day-1“ ;
  ET:scaling_factor = 100 ;
  int ET_QC(Latitude, Longitude) ;
  int ESI_2_WEEK(Latitude, Longitude) ;
  ESI_2_WEEK:units = "none" ;
  ESI_2_WEEK:scaling_factor = 100;
  int ESI_2_WEEK_QC(Latitude, Longitude) ;

## Slide 107: System Description Production – Output Data Files
GETDL3_zz_yyyyddd.vn.fff.gz
zz = domain name: NA (North America)
yyyy = four digit calendar year
ddd = day of year
vn= version number
fff = output format and valid values: grb2, nc or png
GETDL3_NA_2016006.v1.grb2.gz (ET, ESI and other products of North America in GRIB2 format for the version 1.0)
GETDL3_NA_2016006.v1.nc.gz (ET, ESI and other products of North America in NETCDF4 format for the version 1.0)
GETDL3_NA_2016006.v1.png.gz (ET, ESI and other products of North America in PNG format for the version 1.0)

## Slide 108: System Description Production – Status report file
For each GETD run, a status report file is produced to indicate the Processing status of this run.
Each message line in the report file consists of 3 fields, namely the time (yyyymmddhhmmss) of the current message being reported, name of the subprogram that produced the message, and the detailed description of the message.
The detailed description of the message may start with “ERROR” or “WARNING”.
  If “ERROR” appears in the description, the GETD run would be terminated and the final product will not be produced.
  If “WARNING” appears in the description, the GETD run will still continue but the quality of the final product might be affected by fact specified in the warning message.

## Slide 109: System Description Production – Status report
1) % of overall product quality bit in the QF being 1 (not retrieved): If 100%, no retrievals were obtained.
2) % of GOES data availability bit in the QF being 1 (bad data): If 100%, GOES input had problem;
3) mean daily ET of the domain: its time series should be relatively smooth (no abrupt rise or drop);
Note that due to the variations in the GOES inputs and ALEXI model valid outputs, daily ET values could have higher variations than composited ESI values.
4) mean rolling 8day ESI of the domain: its time series should be relatively smooth;
Example of the content in GETDL3_QF2014182.txt:
GETD QF INFO ON: 2014183
GOES valid(%): 33.25
ET valid(%): 32.87
Mean ET(MJ m-2 day-1): 110.13204
Mean ESI 2-week : 0.893
……
Mean ESI 12-week : 1.094

## Slide 110: System Description Unit - Meteorological Forcing Processor
CGMP-CFS
CGLMP
UMD global land mask
Binary data in Alexi domain
Temperature
Pressure
Wind speed
……
CFS in GRIB2

## Slide 111: System Description Unit - Satellite Dataset Processor
INSO-GSIP L2
VIP-VIIRS
SMP
Snow mask
GSIP L2 netcdf4 data
Binary data in Alexi domain
VIIRS EVI/NDVI
CMP
BT (3.9 &11)
Solar insolation
Cloud mask
EVI/NDVI
Snow mask
GOES AREA files
BT 3.9 & 11
GDP

## Slide 112: System Description Unit - Ancillary Dataset Processor
CIP
Clear sky insolation data
LCPP
UMD land cover
Binary data in Alexi domain
AP
Albedo data
Clear sky Solar insolation
Albedo
Land cover

## Slide 113: System Description Unit - ALEXI Core Processor
Binary outputs
Binary inputs
APM
QCF
RIP
ROP
Temperature
Pressure
Wind speed
…...
Solar insolation
……
EVI/NDVI
Snow mask
Outputs
ET
ESI
Radiances and fluxes
ET QC
ESI QC
Radiances and fluxes QC

## Slide 114: System Description Unit - Product Output Processor
Output GRIB2 file
POP
Output NETCDF4 file
Output PNG files
Status report file
Binary outputs
Outputs
ET
ESI
Radiances and fluxes
ET QC
ESI QC
Radiances and fluxes QC

## Slide 115
Introduction
Risks and Actions
System Requirements
System Description
System Test
System Operational Readiness
Summary
115
Outline
Notes: 115
Priyanka: Changed
--“Project Plan” to “Introduction”
--“PDR Report to PDR Risks and Actions”

## Slide 116
Section 5 –
System Test
Rao Venkata

## Slide 117: System Test Objectives
Ensure that all requirements specified for the product processing system and products are satisfied, and the products meet the users’ needs and expectations.

## Slide 118: System Test Description
Each test has been done following the scenario
  Describe the test item
  Show scheduled execution times (cron schedule)
  Show directory listing of output files indicating the file creation time is consistent with the scheduled execution time

## Slide 119: System Test Test Environment
The system test was done at OSPO
  6 CPUs
  2.0 GHz
  16 GB memory
  400 GB additional disk space
  gcc
  PERL
NetCDF, GRIB2 and HDF5 lib were installed
  NetCDF version 4.2
  HDF5 version 1.8.7
  HDF4

## Slide 120: System Test Software installation
The GET-D software was written in FORTRAN 90
To install the source codes, copy the following directories (delivered as a tar file)
  GETD/src
  GETD/script_files
  GETD/lib_packages
  GETD/IDL
Install the libraries
  Follow the instructions in the GETD/lib_packages/README to install all the libraries needed for GETD.
Compile the source codes
  cd GETD/src/make
  Change the paths of libraries in “Makefile”
  Run command “make” from directory “GETD/src/make”
  The executables will be under “/data2/Pgetd/run”

## Slide 121: System Test Software installation
Run the scripts
  Modify the paths of libraries and input/output data in CSHELL scripts under “~/GETD/script_files/”.
  Scripts for daily procedure “run_GETD_by_doy.csh” should be run under “/data2/Pgetd/run” directory.

## Slide 122: System Test Test Items
Daily GETD processing procedures
  Generate the meteorological inputs for the CFS inputs.
  Generate the clear sky morning land surface temperatures from GOES inputs.
  Generate the daily insolation from GSIP inputs.
  Generate the daily LAI from VIIRS inputs.
  Generate the daily Snowmask from IMS inputs.
  Genreate the daily ET and fPET from all the inputs.
  Genreate the daily 2, 4, 8, 12 weekly composite ESI from daily fPET and climatology data.

## Slide 123: System Test Test Items
Daily inputs
  8 daily CFS GRIB2 files for two days.
  Daily GOES EAST and WEST image files from 3 bands.
  24 daily GSIP L2 NETCDF files for two days.
  VIIRS granules/GVF_EVI data files.
  1 snow mask file from IMS.
  Climatology files.
Daily outputs
  1 NETCDF file
  1 GRIB2 file
  1 Ascii file contains the statistics for the output variables
  4 PNG files for comparison

## Slide 124: System Test Daily Procedure
STAR
Driven by cron job.
Determine working day by computer time.
Find paths from CSHELL scripts and
configure files.
Get other parameters from configure files.
Process the input data.
Generate the daily ET and fPET data.
Produce the composite weekly ESI outputs.
OSPO
Driven by cron job.
Determine working day by computer time.
Find paths from CSHELL scripts and
configure files.
Get other parameters from configure files.
Process the input data.
Generate the daily ET and fPET data.
Produce the composite weekly ESI outputs . Tranfer the outputs to DDS and SATEPSANON.

## Slide 125: System Test
CGMP-CFS
run_daily_CFS_STEP1.csh 2015 339
run_daily_CFS_STEP2.csh 2015 339
STAR OSPO

## Slide 126: System Test
INSO-GSIPL2
run_daily_GSIP_STEP1_2.csh 2015 182
run_daily_GSIP_STEP3.csh
STAR OSPO

## Slide 127: System Test
GOES Data Processor (GDP)
run_daily_GOES_STEP1.csh 2015 339
run_daily_GOES_STEP2.csh 2015 339
run_daily_GOES_STEP3.csh 2015 339
STAR OSPO

## Slide 128: System Test
VIP-VIIRS
run_daily_aggEVI.csh
run_daily_VIIRS_EVI.csh 2015 339
run_daily_VIIRS_LAI.csh 2015 339
STAR OSPO

## Slide 129: System Test
SMP
run_daily_SNOWMASK.csh 2015 339
STAR OSPO

## Slide 130: System Test
ROP
run_VLAI_ALEXI.csh 2015 339
STAR OSPO

## Slide 131: System Test
ROP
run_daily_ESI_compute.csh 2015 339
run_daily_ESI_smooth.csh 2015 339
run_daily_ESI_composite.csh 2015 339
run_gen_images.csh 2015 339
STAR OSPO

## Slide 132: System Test sampled products
/data2/Pgetd/data/product/
  GETDL3_NA_2015339.v1.grb2
  GETDL3_NA_2015339.v1.nc
  GETDL3_QF2015339.txt

## Slide 133: System Test Verification of Operational Implementation
GETD products generated at STAR are compared with those produced at OSPO.
The products from STAR and OSPO are very close.
From STAR From OSPO
Notes: 133

## Slide 134
Introduction
Risks and Actions
System Requirements
System Description
System Test
System Operational Readiness
Summary
134
Outline
Notes: 134
Priyanka: Changed
--“Project Plan” to “Introduction”
--“PDR Report to PDR Risks and Actions”

## Slide 135
Section 6 –
Operational Readiness Presented by Hanjun Ding

## Slide 136: System Operational Readiness Production Environment
Two LINUX Servers for GET-D – GSRDEV and GSRPROD
  Development and Backup – GSRDEV
      Development and testing on GSRDEV
      Pre-operational code received from STAR has been well tested.
  Production – GSRPROD
      GET-D will be run to generate the operational products on GSRPROD
      The products will be distributed to users through ESPC Data Distribution System (DDS) and SATEPSANON

## Slide 137: System Operational Readiness Input Data Sources
GOES East/West Imagery
GSIP Insolation
VIIRS EVI from NDE GVF
Ancillary Data for Product Generation
  CFS from NCEP
  Snow mask from NOAA IMS
  Land cover from UMCP
  Albedo from MODIS

## Slide 138: System Operational Readiness Input Data Sources
Name | Category | Source | FORMATS | Description
Brightness temperature | Satellite observation | GOES | McIDAS | GOES East/West Imagery; 11micron/3.9 micron brightness temperature
Insolation | Satellite observation | GSIP | NetCDF4 | GSIP real time insolation
Vegetation Index | Satellite observation | VIIRS | HDF5 | VIIRS EVI
Snow mask | Satellite observation | NOAA IMS | ASCII | IMS Daily Northern Hemisphere Snow and Ice Analysis
Air temperature | Meteorological data | CFS | GRIB2 | Surface and pressure level profiles
Specific humidity | Meteorological data | CFS | GRIB2 | Surface and pressure level profiles
Geopotential height | Meteorological data | CFS | GRIB2 | Surface and pressure level profiles
Wind speed | Meteorological data | CFS | GRIB2 | Surface
Downwelling longwave radiation | Meteorological data | CFS | GRIB2 | Surface
Land Cover | Ancillary data | University of Maryland | BIN | Land cover classes in 1km resolution (static)
Albedo | Ancillary data | MODIS | BIN | Surface Albedo from MODIS (static)
Clear day insolation | Ancillary data | GSIP | NetCDF4 | Clear day insolation (static)

## Slide 139: System Operational Readiness System Outputs
Variables | Source | Spatial Domain | RESOLUTION / FORMATS | Description
ET Product with QC | GET_D | Northern America | 8 km NetCDF, GRIB2 | Daily ET Map
ESI Products with QC | GET-D | Northern America | 8 km NetCDF, GRIB2 | 2, 4, 8, 12-week Composite Drought map
Flux Products with QC | GET-D | Northern America | 8 km NetCDF, GRIB2 | Daily Sensible Heat and Soil Heat Flux Map
Radiance Products with QC | GET-D | Northern America | 8 km NetCDF, GRIB2 | Daily Short Wave Down; Long wave Down, Long wave Up and Net Radiation Map

## Slide 140
System Operational Readiness Data Flow Diagram
GEODIST2/3 (GOES)
NDE Server (EVI)
GSRPROD(GSIP)
GSRPROD Production
GET-D products in netCDF4 and GRIB2
OTHER USERS
NCEP/EMC
(ET)
NCEP/CPC
(ESI)
DDS/satepsanon
GET-D products in
netCDF4 and GRIB2
USDA
NDMC/NIDIS
(ESI)
External User Zone
Distribution Zone (DMZ)
Development Zone
Production Zone
*: PE - Production Environment
DDS
Ancillary data
Notes:   Grouped and SmartArt version

## Slide 141: System Operational Readiness IT System Architecture

## Slide 142: System Operational Readiness Users of Products
  NWS/NCEP EMC POC (ET): Mike Ek, Youlong Xia
  NWS/NCEP CPC POC (ESI): Kingtze Mo, Jin Huang
  NDMC-UNL POC (ESI): Brain Wardlow, Mark Svoboda
  USDA POC (ESI): Marth Anderson (ARS)
  Zhengwei Yang (NASS)
  Curt Reynolds (FAS)

## Slide 143: System Operational Readiness Production
The GET-D product system is running in VMWare Linux system.
GET-D products (ET and ESI) will be generated from GSRPROD.
GOES East/West Imagery will be pulled from GEODIST2/3; VIIRS EVI will be pulled from NDE server; Iosolation will be pulled from GSRPROD.
CFS, Snow mask, Land cover, Albedo and Clear day Insolation will be pulled from DDS.
The products are in netCDF4 and GRIB2 formats.

## Slide 144: System Operational Readiness Dissemination
DDS for real time users
  GET-D products in NetCDF4 and GRIB2 formats
Satepsanone
  GET-D products in NetCDF4 format

## Slide 145: System Operational Readiness Monitoring
Quality Monitoring
  The GET-D Product files include overall quality control flags and quality summary level metadata
  ESPC Monitoring project includes GET-D and it will be available soon.
Performance Monitoring
  GET-D is running in VMWare Linux system (GSRdev & GSRprod). The running status is monitored by ESPC maintenance personnel in 24x7.

## Slide 146: System Operational Readiness Maintenance (1/3)
OSPO Products Area Lead – Hanjun Ding
OSPO QA Lead – Zhaohui Cheng
OSPO ESPC Operation Lead - Donna McNamara
OSPO O&M Team
  Rao Venkata
  Bob Potash
STAR Science Maintenance Team
  Jerry Zhan
  Zhengpeng Li

## Slide 147: System Operational Readiness Maintenance (2/3)
O&M Procedures
  Operation Procedure and System Maintenance Manual will follow ESPC O&M procedures.
  GET-D operation system will follow ESPC CM and security procedures.
  The primary and backup maintenance personnel have been identified to cover normal maintenance needs.
  The PAL will work with STAR scientists for any science maintenance needs when identified.
Operation Support
  ESPC Operational Support Team

## Slide 148: System Operational Readiness Maintenance (3/3)
Maintenance Supports
  Processing failures due to machines problems such as disk storage or over loaded CPU.
  Processing terminated (or hung up) abnormally such as delayed or problematic inputs, bugs.
  Product dissemination problems
  Product degradation due to channel/sensor/satellite problems, …etc.
  Adding or deleting satellite data according to availability.
  Algorithm updates/enhancements implementation
Emergency Recovery Capability
  GET-D may not be run at the CIP (Critical Infrastructure Protection) facility when it is operational.

## Slide 149: System Operational Readiness QA – Code Standards
The GET-D has passed through Code Review
  OSPO leads the Code Review for coding standards and security
  All the open items from code review have been closed
  Results have been documented in Code Review Report
  The code review report, as a ORR review artifact, can be found at: ftp://satepsanone.nesdis.noaa.gov/GET-D/

## Slide 150: System Operational Readiness QA – CM and IT security
Product implementation
  Implementation on parallel test environment is tasked and managed by Change Requests (CCR3234, Title: Implementation of GOES ET and Drought Products (GET-D)).
  Software CM follows ESPC Software Configuration Management Process and Procedures Manual.
Security Procedures
  SIA (CCR3234) has been performed for GET-D before the system is promoted into operation.
Documents will be under the CM control at OSPO

## Slide 151: System Operational Readiness QA – Documentation
SPSRB Required Docs
  Completed the draft User Manuals, System Maintenance Manual, ATBD
  Need be finalized before the GET-D is operational

## Slide 152: System Operational Readiness Archive
GET-D Products Archive
  An initial request has be submitted to NCEI/CLASS through its online Advanced Tracking and Resource Tool (ATRAC) in January 2014
  The request was denied in February 2015.
  Still working with NCEI management to get the request approved.

## Slide 153: System Operational Readiness User Readiness (1/2)
Data Access
  GET-D products will be put on DDS for real time users.
  Non-real time users will get the products from ESPC ftp site ftp://satepsanone.nesdis.noaa.gov/GETD/TEST.
  Real-time data will be sent to DDS for NCDC CLASS.
Acceptance of Product
  Already use GET-D product generated from NCEP.
  Already reviewed test data.

## Slide 154: System Operational Readiness User Readiness (2/2)
Training
  User manuals will be made available to all users
    No specific training from OSPO is planned. Products are in self-descripted NetCDF format.
  ESPC Operator
    GET-D will be monitored by ESPC help desk. No training is needed.

## Slide 155: System Operational Readiness Summary
The system is ready for operations
The documentation will be completed by the time the GET-D is officially declared operational (final touches need to be done to the documents)
The users are ready to receive and use the data

## Slide 156
Introduction
Risks and Actions
System Requirements
System Description
System Test
System Operational Readiness
Summary
156
Outline
Notes: 156
Priyanka: Changed
--“Project Plan” to “Introduction”
--“PDR Report to PDR Risks and Actions”

## Slide 157
Risk and Actions have been reviewed
Requirements and their Allocations have been reviewed
System Description and Test have been reviewed
Products Quality Readiness have been reviewed
Operation Readiness has been reviewed
User Readiness has been reviewed
157
Summary
Notes: 157
Priyanka: Changed
--“Project Plan” to “Introduction”
--“PDR Report to PDR Risks and Actions”

## Slide 158
Operational Phase
  SPSRB Decision Briefing: February 17, 2016
  Operational Commencement: March 31, 2016
158
Next Step
Notes: 158
Priyanka: Changed
--“Project Plan” to “Introduction”
--“PDR Report to PDR Risks and Actions”

## Slide 159
The review is now open for free discussion
159
Open Discussion
Notes: 159
Priyanka: Changed
--“Project Plan” to “Introduction”
--“PDR Report to PDR Risks and Actions”