## Slide 1: Operational Readiness Review eTRaP Upgrade-GPM/GMI
Prepared by:
Liqun Ma1, Bob Glassberg2 , Bob Kuligowski3
1 NOAA/NESDIS/OSPO
2 SGT
3 NOAA/NESDIS/STAR
February 21, 2017
1
Notes: 1
LM: update the date
BK: Changed the date to February 27
GHE Operational Readiness Review

## Slide 2: Review Agenda
2
Introduction
Risks and Actions
Requirements
System Description
System Test
System Operational Readiness
Summary
2
2
Notes: 2

## Slide 3: Outline
3
Introduction
Risks and Actions
System Requirements
System Description
System Test
System Operational Readiness
Summary
3
3
Notes: 3

## Slide 4: Introduction Bob Kuligowski NOAA/NEDSIS/STAR
4
4
Notes: 4

## Slide 5: eTRaP Background (1/3)
Tropical Rainfall Potential (TRaP) is a forecast of rainfall from a tropical cyclone based on extrapolating satellite-derived instantaneous rain rate estimates along the predicted storm track.
Ensemble TRaP (eTRaP) uses an ensemble of TRaPs based on multiple satellite-derived rain rates and predicted storm tracks to derive a maximum likelihood rainfall forecast and probability of exceeding specified rainfall accumulation thresholds.
Forecasts are produced for the 0-24 h time frame at 6-h intervals with initialization times of 0, 6, 12, and 18 UTC. The code is run 3 h after initialization time and output is distributed ~4 h after initialization time.
5

## Slide 6: eTRaP Background (2/3)
eTRaP became an operational product at OSPO in 2009
The retirement of the SSM/I and TMI and loss of AMSR-E degraded eTRaP availability, particularly over the Atlantic Basin, because of an insufficient number of ensemble members.
Subsequent improvements to eTRaP include
  Adding rainfall rates from new instruments (SSMIS, GHE, ATMS, AMSR2) to replace retired / lost instruments (SSM/I, TRMM, AMSR-E)
  Calibrating the ensemble probabilities to remove bias
6
Notes: BK: Deleted “has” after “AMSR-E” in second bullet since availability is no longer degraded.

## Slide 7: eTRaP Background (3/3)
Additional improvements to eTRaP are ongoing, including
  Additional instruments (GMI; the subject of this review)
  Addition of R-CLIPER to the ensemble
7
Notes: BK: Deleted reference to orographic correction since we aren’t going to implement it because the test results didn’t warrant it.

## Slide 8: Project Objectives
Add TRaPs produced using GPM GMI rain rates from the NASA PPS
  First, determine the optimal weighting of TRaPs using the GMI rain rates based on their skill relative to other MW TRaPs.
  Adding GPM GMI rain rates must improve the reliability and / or accuracy of eTRaP. DE.
8

## Slide 9
IPT Lead: Bob Kuligowski (STAR)
PAL and IPT Backup Lead: Liqun Ma (OSPO)
Science Advisor: Elizabeth Ebert (CAWCR - Melbourne, Australia)
NESDIS team:
STAR: Ralph Ferraro
OSPO: Liqun Ma, Limin Zhao, Nancy Merkle (Web Coordinator), Robert Glassberg (SGTPrimary Programmer), Clay Davenport (SGT Backup Programmer)
OSGS: Kathryn Shontz
NWS team:
NCEP/TPC/NHC: Mark DeMaria (RCLIPER)
User team
Leads: Michael Turk, Alan Schwartz
Others: Dan Brown (TPC), Mark Klein (WPC), Greg Shelton (West Gulf RFC), Alipate Waqaicelua (Nadi Regional Specialized Meteorological Centre (RSMC)), Andrew Burton (Perth TCWC)
Product Oversight Panel: PREPOP
Project Stakeholders
9
Notes:   BK: Replaced “HPC” with “WPC”.
  LM: should we delete OAR team since we aren’t going to implement it?
  BK: Good point; I deleted it

## Slide 10
SAB
  Mike Turk
WPC
  Mark Klein
Project Stakeholders – Customers / Users
10
Notes: BK: Replaced “HPC” with “WPC”

## Slide 11
OSPO ESPC
  Run eTRaP system
  Distribute eTRaP products to users
  Perform routine product quality monitoring and maintenance
OSPO Products Area Lead – Liqun Ma
OSPO QA Lead – Zhaohui Cheng
ESPC O&M Team
  Robert Glassberg
STAR Science Maintenance Team
  Bob Kuligowski
  Elizabeth Ebert
Project Stakeholders – O&M
11

## Slide 12
Apr 16: Development Phase Begins
  Apr 16: IPT Lead informed to begin product development
  Apr 16: Development processing system defined
  Oct 16: Test cases processed
  Oct 16: Code is prepared for implementation
Oct 16: Pre-operational Phase Begins
  Oct 16: Operational and backup processing capabilities in place
  Oct 16: Pre-operational product output evaluated & tested
  Nov 16: System/Algorithm Readiness Review
  Nov 16: Code transitions to operations; all documentation is complete
  Dec 16: Operational and backup capabilities reach ops status
  Dec 16: Operational Readiness Review
  Dec 16: Update SPSRB Oversight Panel(s) on product status
  Dec 16: Brief OSPO capability is ready to operational
Dec 16: Operational Phase Begins
  Jan 17: SPSRB manager and secretaries notified update/upgrade went into operations.
    SPSRB Secretaries/manager update the SPSRB product metrics web pages
  Jan 17: OSGS updates Satellite Products database
Project Plan
12
Notes: BK: Should we change these dates to reflect the actual dates or leave them as is to reflect the project plan?

## Slide 13
Schedule (Milestones)
  Critical Design Review – waived
  Algorithm Change Package delivered to OSPO – 10/27/2016
  Algorithm Readiness Review – waived
  Software Review – waived
  Operational Readiness Review – 02/21/2017
  Transition to operations – 4/2017
Project Plan - Milestones
13

## Slide 14: ORR – Review Objectives
Review Project Plan
Review the open Risks and Actions
Review the System Requirements Updates
Review the System Description
Review the System Test Report
Review System Operational Readiness
14
Notes: 14

## Slide 15: ORR Reviewers
ORR Review Leads
  Antonio Irving, Zhaohui Cheng and Liqun Ma
ORR Review Team
  Liqun Ma (OSPO/SPSD)
  Zhaohui Cheng (OSPO/SPSD)
  Antonio Irving (OSPO/SPSD)
  Donna McNamara (OSPO/MOD)
  Bob Kuligowski (STAR)
ORR Review Consultants
  Kathryn Shontz(OSGS)
15
Notes: 15

## Slide 16: ORR Guidelines and Checklist
Guidelines for ORR review is the OSPO QA process asset
  ORR reviewers can access this document at
  ftp://satepsanone.nesdis.noaa.gov/testTRAP/ORR_DOC
The ORR Review Check List and ORR related documents are available at:
  ftp://satepsanone.nesdis.noaa.gov/testTRAP/ORR_DOC
16
Notes: 16

## Slide 17: Outline
Introduction
Risks and Actions
System Requirements
System Description
System Test
System Operational Readiness
Summary
17
Notes: 17

## Slide 18: Risks and Actions Bob Kuligowski NESDIS/STAR
18
Notes: 18

## Slide 19
Risks and Actions
There are no remaining risks from previous reviews.
19
Notes: Updated stats

## Slide 20: ORR – Entry Criteria
Entry # 1 - The ORR reviewers have access to the review version of the following artifacts
  Requirements Allocation Document (RAD)
  Review Item Disposition Spreadsheet (RID)
  Operational Readiness Review Document (ORRD)
Entry # 2 - The ORR reviewers have access to the old version of SPSRB Documents
  User Manuals
  System Maintenance Manual
Entry # 3 - The ORR reviewers have access to the review version of the Operations Procedure
20
Notes: BK: Changed Entry #4 to #3 since there was no #3
GHE Operational Readiness Review
20

## Slide 21: ORR – Exit Criteria
Exit # 1 - All open items in RID have been satisfactorily disposed of.
Exit # 2 - The updated RAD is satisfactory.
Exit # 3 - The SPSRB documents (UM, SMM, ICD, SDD, and OM) have been reviewed and are deemed to be satisfactory.
Exit # 4 - Test and validation results are satisfactory.
Exit # 5 - The operation readiness are satisfactory.
Exit # 6 - The security impact assessment (SIA) has been completed. -- deferred to Operational Decision Briefing
21
Notes: GHE Operational Readiness Review
21

## Slide 22: Outline
Introduction
Risks and Actions
System Requirements Updates
System Description
System Test
System Operational Readiness
Summary
22
Notes: 22

## Slide 23: System Requirements
Bob Kuligowski
23
Notes: 23

## Slide 24: Requirements Overview
All eTRaP requirements are documented in the RAD:
http://www.star.nesdis.noaa.gov/smcd/emb/bobk/eTRaP_docs/ORR/eTRaP_Requirements_Allocation_Document_v2.3.docx
Text highlighted
  Changes/updates to requirements since the last review are in Green.
  Requirements specific to this upgrade of eTRaP are in Brown
24

## Slide 25: Requirement #0
ETRAP-R 0.0: The eTRaP Upgrade project shall adopt the standard practices of the SPSRB Review Process for transition of a product from research to operations.
Driver: SPSRB transition to operations process. Since this is an enhancement to an existing operational system, only the process steps related to modifying an existing system need be followed.
25

## Slide 26: Requirement #0
ETRAP-R 0.1: The eTRaP Upgrade project reviews shall be tailored.
  This derived requirement has been adopted to mitigate schedule risk by eliminating the overhead of preparing review slide packages and reports.
ETRAP-R 0.1.1: The Requirements Review (RADR), Preliminary Design Review (PDR), Critical Design Review (CDR), and the Unit Test Readiness Review (TRR) for the S-NPP upgrade of eTRaP have been waived.
  This derived requirement has been adopted to mitigate schedule risk by eliminating the overhead of preparing a RADR, PDR, CDR, and TRR slide packages and reports. The Technical risk is assessed as Low because the update to the system only involves processing a new data set.
26

## Slide 27: Requirement #0
ETRAP-R 0.1.2: There shall be an Algorithm Readiness Review (ARR) for the S-NPP upgrade of eTRaP.
  This derived requirement has been adopted from the SPSRB Review process.
ETRAP-R 0.1.3: There shall be an Algorithm Readiness Review Report (ARRR) for the S-NPP upgrade of eTRaP.
  The ARRR is one of the exit criteria for ARR.
27

## Slide 28: Requirement #0
ETRAP-R 0.1.4: There shall be an Operational Readiness Review (ORR) for the S-NPP upgrade of eTRaP.
  This derived requirement has been adopted from the SPSRB Review process.
ETRAP-R 0.1.5: There shall be an Operational Readiness Review Report (ORRR) for the S-NPP upgrade of eTRaP.
  The ORRR is one of the exit criteria for ORR.
28

## Slide 29: Requirement #0
ETRAP-R 0.1.6: The Requirements Review (RADR), Preliminary Design Review (PDR), Critical Design Review (CDR), and Unit Test Readiness Review (UTRR) for the AMSR2 upgrade of eTRaP have been waived.
    This derived requirement has been adopted to mitigate schedule risk by eliminating the overhead of preparing a RADR, PDR, CDR, and TRR slide packages and reports. The Technical risk is assessed as Low because the update to the system only involves processing a new data set.
29
Notes: Priyanka: Requirements 0.1.7 to 0.1.11 to be reviewed at the R-CLIPER upgrade review

## Slide 30: Requirement #0
ETRAP-R 0.1.7: There shall be an Algorithm Readiness Review (ARR) for the AMSR2 upgrade of eTRaP.
  This derived requirement has been adopted from the SPSRB Review process.
ETRAP-R 0.1.8: There shall be an Algorithm Readiness Review Report (ARRR) for the AMSR2 upgrade of eTRaP.
  The ARRR is one of the exit criteria for ARR.
30

## Slide 31: Requirement #0
ETRAP-R 0.1.9: There shall be an Operational Readiness Review (ORR) for the AMSR2 upgrade of eTRaP.
  This derived requirement has been adopted from the SPSRB Review process.
ETRAP-R 0.1.10: There shall be an Operational Readiness Review Report (ORRR) for the AMSR2 upgrade of eTRaP.
  The ORRR is one of the exit criteria for ORR.
31

## Slide 32: Requirement #0
ETRAP-R 0.1.11: There shall be a Critical Design Review (CDR) for the R-CLIPER and orography upgrade of eTRaP.
  This upgrade will require design upgrades that will be presented at the CDR.
ETRAP-R 0.1.12: There shall be a Critical Design Review Report (CDRR) for the R-CLIPER and orography upgrade of eTRaP.
  The CDRR is one of the exit criteria for CDR.
32

## Slide 33: Requirement #0
ETRAP-R 0.1.13: There shall be an Algorithm Readiness Review (ARR) for the R-CLIPER and orography upgrade of eTRaP.
  This derived requirement has been adopted from the SPSRB Review process.
ETRAP-R 0.1.14: There shall be an Algorithm Readiness Review Report (ARRR) for the R-CLIPER and orography upgrade of eTRaP.
  The ARRR is one of the exit criteria for ARR.
33
Notes: Priyanka: Requirements 0.1.7 to 0.1.11 to be reviewed at the R-CLIPER upgrade review

## Slide 34: Requirement #0
ETRAP-R 0.1.15: There shall be a eTRaP R-CLIPER Upgrade Operational Readiness Review (ORR).
  This derived requirement has been adopted from the SPSRB Review process.
ETRAP-R 0.1.16: There shall be a eTRaP R-CLIPER Upgrade Operational Readiness Review Report (ORR).
  The ORRR is one of the exit criteria for ORR.
34
Notes: Priyanka: Requirements 0.1.7 to 0.1.11 to be reviewed at the R-CLIPER upgrade review

## Slide 35: Requirement #0
ETRAP-R 0.1.17: The Requirements Review (RADR), Preliminary Design Review (PDR), Critical Design Review (CDR), Unit Test Readiness Review (UTRR), and Algorithm Readiness Review (ARR) for the GMI upgrade of eTRaP have been waived.
    This derived requirement has been adopted to mitigate schedule risk by eliminating the overhead of preparing RADR, PDR, CDR, UTRR, and ARR slide packages and reports. The Technical risk is assessed as Low because the update to the system only involves processing a new data set.
35
Notes: Priyanka: Requirements 0.1.7 to 0.1.11 to be reviewed at the R-CLIPER upgrade review

## Slide 36: Requirement #0
ETRAP-R 0.1.18: There shall be an Operational Readiness Review (ORR) for the GMI upgrade of eTRaP.
  This derived requirement has been adopted from the SPSRB Review process.
ETRAP-R 0.1.19: There shall be an Operational Readiness Review Report (ORRR) for the GMI upgrade of eTRaP.
  The ORRR is one of the exit criteria for ORR.
36
Notes: Priyanka: Requirements 0.1.7 to 0.1.11 to be reviewed at the R-CLIPER upgrade review

## Slide 37: Requirement #0
ETRAP-R 0.2: The Requirements Allocation Document (RAD) shall be created and maintained by the eTRaP development team.
  This derived requirement has been adopted from the SPSRB Review process. The RAD will follow document standards stated in EPL v3 process asset DG-6.2
ETRAP-R 0.3: The Review Item Disposition (RID) spreadsheet shall be created and maintained by the eTRaP development team.
  This derived requirement has been adopted from the SPSRB Review process.
ETRAP-R 0.4: Configuration Management shall be implemented.
  OSPO will CM the code and associated documents using Subversion.
37

## Slide 38: Requirement #1
ETRAP-R 1.0: The Ensemble Tropical Rainfall Potential (eTRaP) forecast of rainfall for a tropical system shall be upgraded.
Driver: This basic requirement is traced to user needs as stated in SPSRB User Requests: SPSRB user request # 1001-0001 “eTRaP Upgrade” by NWS/NCEP/WPC (formerly HPC).
38
Notes: Replaced “HPC” with “WPC (formerly HPC)”

## Slide 39: Requirement #1
ETRAP-R 1.0.1: The rain rates generated from the DMSP SSMIS sensor shall be incorporated into the eTRaP ensemble.
ETRAP-R 1.0.2: The rain rates generated from the Global Hydro-Estimator shall be incorporated into the eTRaP ensemble.
ETRAP-R 1.0.3: The rain rates generated from the S-NPP ATMS sensor shall be incorporated into the eTRaP ensemble.
ETRAP-R 1.0.4: The rain rates generated from the GCOM-W AMSR2 sensor shall be incorporated into the eTRaP ensemble.
39

## Slide 40: Requirement #1
ETRAP-R 1.0.5: The rain rates generated by R-CLIPER model shall be incorporated into the eTRaP ensemble.
ETRAP-R 1.0.6: The rain rates generated from the GPM GMI sensor shall be incorporated into the eTRaP ensemble.
40

## Slide 41: Requirement #1
ETRAP-R 1.1: The generated TRaP forecasts shall be combined in a weighted simple ensemble to produce quantitative precipitation forecasts and probabilistic forecasts of heavy rain exceeding several thresholds.
  Weights depend on the latency of the TRaP (greater weight for more recent input) and optionally for the sensor used.
ETRAP-R 1.2: The probabilities generated by eTRaP shall be adjusted to remove bias.
ETRAP-R 1.3: The eTRAP system shall take into account the impact of topography of the region and cyclone climatology using NHC Rainfall Climatology persistence model (RCLIPER) in the individual ensemble members to improve accuracy of the forecast.
41

## Slide 42: Requirement #1
ETRAP-R 1.4: The eTRaP rain rates shall be generated for the entire globe for 5 time intervals (0-6, 6-12, 12-18, 18-24, and 0-24 h).
  User request
ETRAP-R 1.4.1: The eTRaP algorithm shall be applied to data from NOAA-18, NOAA-19, MetOp-A/B, DMSP F16, DMSP F17, DMSP F18, GOES-E, GOES-W, METEOSAT-7, METEOSAT-10, Himawari-8, S-NPP, GCOM-W, and GPM satellites, plus R-CLIPER.
42
Notes: BK: Replaced “GMI” with “GPM”.

## Slide 43: Requirement #1
ETRAP-R 1.5: Accuracy of the eTRaP rain rates shall be such that to achieve reduced random errors in rain field, more accurate location and intensity of maximum rainfall.
  User Request.
ETRAP-R 1.6: Latency (average elapsed time from data observation to delivery of the product to the user) shall not exceed 2.5 hours (assuming receipt of blind orbits).
  User Request.
43

## Slide 44: Requirement #1
ETRAP-R 1.7: Timeliness (Latest time after observation by which a product can be delivered and still be useful to the customer) shall be 4.5 hours (assuming receipt of blind orbits).
  User Request.
ETRAP-R 1.8: The output format for eTRaP product shall be McIDAS Area file, ASCII, GRiB2 and GIF.
  User Request; ASCII format requested by WPC and NCEI will be provided in addition to McIDAS and GIF formats.
44
Notes: BK: Replaced “HPC” with “WPC”.

## Slide 45: Requirement #1
ETRAP-R 1.9: The eTRaP developers shall perform validation and verification of the eTRaP rain rate product and exceedence probabilities.
ETRAP-R 1.9.1: The eTRaP developers shall perform tests to verify functional performance of the code that produces the eTRaP Product.
  Tests will be conducted.
45

## Slide 46: Requirement #1
ETRAP-R 1.9.2: The eTRaP developers shall verify that the eTRaP product files are generated correctly.
  This will be done as part of the tests.
ETRAP-R 1.9.3: The eTRaP developers shall verify the error handling capability of the pre-operational system.
  Already done in the existing system.
46

## Slide 47: Requirement #1
ETRAP-R 1.10: The eTRaP rain rates shall be compared with in situ measurements.
ETRAP-R 1.10.1: Metrics for assessing eTRaP performance shall be:
  Quantitative Precipitation Forecasts (QPFs) (maximum rainfall, spatial rainfall pattern
    Bias (mean difference), root mean square error, correlation coefficient
    Frequency bias, probability of detection, false alarm ratio, equitable threat score
    Location, volume, and pattern errors estimated using Contiguous Rain Area (CRA) verification
  Probabilistic forecasts of rain exceeding various thresholds:
    Reliability diagrams
    Relative operating characteristics (ROC) and relative value diagrams
  Brier score, ranked probability score
47

## Slide 48: Requirement #1
ETRAP-R 1.10.2: The eTRaP developers shall produce and distribute eTRaP test sample products to the user community.
  To ensure user acceptance of the product.
48

## Slide 49: Requirement #2
ETRAP-R 2.0: The eTRaP processing system shall have a data ingest capability.
Driver: This basic requirement is traced to algorithm input needs, as documented in the ATBD.
49

## Slide 50: Requirement #2
ETRAP-R 2.1: The upgraded eTRaP system shall ingest DMSP SSMIS TRaP forecast data in McIDAS AREA format.
ETRAP-R 2.2: The upgraded eTRaP system shall ingest GHE forecast data in McIDAS AREA format
ETRAP-R 2.3: The upgraded eTRaP system shall ingest S-NPP ATMS TRaP forecast data in McIDAS AREA format.
50

## Slide 51: Requirement #2
ETRAP-R 2.4: The upgraded eTRaP system shall ingest GCOM-W AMSR2 TRaP forecast data in McIDAS AREA format.
ETRAP-R 2.5: The upgraded eTRaP system shall produce and use R-CLIPER forecast data in McIDAS AREA format.
ETRAP-R 2.6: The upgraded eTRaP system shall ingest GPM GMI TRaP forecast data in McIDAS AREA format.
51

## Slide 52: Requirement #3
ETRAP-R 3.0: The eTRaP processing system shall have QC monitoring capability.
Driver: This basic requirement is traced to an OSPO need for QC monitoring.
52

## Slide 53: Requirement #3
ETRAP-R 3.1: The eTRaP processing system outputs shall include overall quality control flags and quality summary level metadata.
  Needed for distribution, archive, quality control, and post-processing in the products files. eTRaP code will generate metadata for this purpose.
ETRAP-R 3.2: The eTRaP system shall be capable of monitoring input data latency and overall quality.
  Current operational eTRaP system is monitoring input data latency and update the product every hour.
53

## Slide 54: Requirement #3
ETRAP-R 3.3: The eTRaP system shall be capable of monitoring product latency.
ETRAP-R 3.4: The eTRaP system shall produce real-time imagery files for visual inspection of output data files
ETRAP-R 3.5: The eTRaP system shall be capable of monitoring product distribution status to ensure that the data/products are successfully available for transfer to the user community.
  There is an eTRaP system monitoring webpage which monitors all system processing stages including distribution status.
54

## Slide 55: Requirement #3
ETRAP-R 3.5.1: Each log file shall include all runtime error messages.
  Error messages will include system messages and error conditions written by the code.
ETRAP-R 3.5.2: The log file shall indicate whether or not the run was completed without error.
  Code will write this message.
55

## Slide 56: Requirement #4
ETRAP-R 4.0: The eTRaP developers shall produce a fully functional pre-operational system in the STAR Development Environment.
Driver: This basic requirement is traced to an OSPO need for a fully functional system ready for integration and system testing.
56

## Slide 57: Requirement #4
ETRAP-R 4.1: The STAR Development Environment shall host the pre-operational system.
  Pre-operational system is to be developed in this environment
ETRAP-R 4.1.1: The STAR Development Environment shall include a Linux machine.
  Needed for the code.
ETRAP-R 4.1.2: The STAR Development Environment shall have storage of 520KB for code storage, 400KB for input data, 80MB for output data and 130MB RAM .
57

## Slide 58: Requirement #4
ETRAP-R 4.1.3: The STAR Development Environment shall include the McIDAS graphical/imaging program.
  Needed for running the code.
ETRAP-R 4.1.4: The STAR Development Environment shall include FORTRAN programming language/compiler and Perl, Bash, korn scripting languages.
  Needed for running the code.
58

## Slide 59: Requirement #4
ETRAP-R 4.2: The STAR Development Environment shall be capable of hosting unit tests.
ETRAP-R 4.2.1: The pre-operational system shall include all processing code and all input test data needed to conduct unit tests
  Complete unit test of each stage of the pre-operational system is expected before delivery to OSPO
59

## Slide 60: Requirement #5
ETRAP-R 5.0: The upgraded eTRaP system shall be able to run on the existing OSPO Operational environment running eTRaP.
Driver: eTRaP is currently running operationally on GEOPROD3 in OSPO.
60

## Slide 61: Requirement # 5
ETRAP-R 5.1: The upgraded eTRaP system shall use the RedHat Linux platform for the processing task required.
ETRAP-R 5.2: Disk storage for the input data (60 – 400 KB for each storm run) shall be established within OSPO.
  Input data will be retained for 2 days and this includes the additional storage on 18.5 KB required for the AMSR2 input.
ETRAP-R 5.3: The upgraded eTRaP system shall use the Fortran90 (Absoft90) compiler.
61

## Slide 62: Requirement #5
ETRAP-R 5.4: The upgraded eTRaP system shall use the Perl, Bash and korn scripting languages and IDL and McIDAS libraries.
ETRAP-R 5.5: The upgraded eTRaP system shall be monitored by ESPC helpdesk monitoring tool TIDAL.
ETRAP-R 5.6: The eTRaP outputs shall be stored in operational environment for at least 7 days for distribution.
62

## Slide 63: Requirement #5
ETRAP-R 5.6.1: The total storage of data for distribution shall be 80MB.
  This includes 30 each of McIDAS, GIF and ASCII files.
ETRAP-R 5.6.2: The eTRaP products shall be distributed using the ESPC Data Distribution Server(DDS) / Product Distribution and Access (PDA) and using a web server to the user community at http://www.ssd.noaa.gov/PS/TROP/etrap.html.
  Standard procedure for this user community.
63
Notes: BK: Added “Product Distribution and Access (PDA)”

## Slide 64: Requirement #6
ETRAP-R 6.0: The eTRaP pre-operational system shall be transitioned from the STAR Development Environment to the OSPO Environment.
Driver: This basic requirement is traced to an OSPO need for a fully functional system in its Environment.
64

## Slide 65: Requirement #6
ETRAP-R 6.1: The pre-operational system shall include all processing code and all input test data needed to reproduce the unit tests.
  For system testing. A complete system test of the integrated pre-operational system is expected before delivery to OSPO Environment.
ETRAP-R 6.2: The integrated pre-operational system shall include all output data produced by the unit tests.
  Needed by OSPO to verify the system tests in its Environment.
65

## Slide 66: Requirement #6
ETRAP-R 6.3: The eTRaP development team shall set up an internal FTP site for transferring the pre-operational system to OSPO as a tar file on a STAR server that is accessible to OSPO.
ETRAP-R 6.3.1: The eTRaP development team shall ensure that the OSPO PAL has the information needed to acquire the pre-operational system as a tar file.
66

## Slide 67: Requirement #7
ETRAP-R 7.0: STAR shall deliver updated eTRaP documents to OSPO.
Driver: This basic requirement is traced to an OSPO need for documentation to support operations, maintenance, and distribution
67

## Slide 68: Requirement #7
ETRAP-R 7.1: The eTRaP document package shall include a User’s Manual (UM)
  The existing eTRaP UM following the SPSRB Version1 document standards will be updated.
ETRAP-R 7.2: The eTRaP document package shall include a System Maintenance Manual (SMM)
  The existing eTRaP SMM following the SPSRB Version1 document standards will be updated.
68

## Slide 69: Requirement #7
ETRAP-R 7.3: The eTRaP document package shall include an Interface Control Document (ICD).
  The existing eTRaP ICD following the SPSRB Version1 document standards will be updated.
ETRAP-R 7.4: The eTRaP document package shall include a System Description Document (SDD).
  The existing eTRaP SDD following the SPSRB Version1 document standards will be updated.
69

## Slide 70: Requirement #7
ETRAP-R 7.5: The eTRaP document package shall include an Operations Manual (OM).
  The existing eTRaP OM following the SPSRB Version1 document standards will be updated.
ETRAP-R 7.6: The eTRaP document package shall include an updated Archive Agreement.
70

## Slide 71: Requirement #8
ETRAP-R 8.0: The eTRaP products shall be archived.
  Daily tar file for each storm will be sent to NCEI; no changes to archive plan for eTRaP upgrades.
71

## Slide 72: Requirement #8
ETRAP-R 8.1: Distribution of the Archive Products to NCEI shall be in accordance with a Data Submission Agreement (DSA).
ETRAP-R 8.2: The eTRaP files and associated metadata shall be archived by NCEI .
  NCEI will generate the metadata for the eTRaP during archival of the products. Archive users will obtain eTRaP data from the NCEI servers.
72

## Slide 73: Requirement #9
ETRAP-R 9.0: The eTRaP system shall comply with OSPO Code Review Security check lists.
Driver: OSPO code standards and OSPO security requirements
73

## Slide 74: Requirement #9
ETRAP-R 9.1: The eTRaP system shall comply with OSPO data integrity check list.
  OSPO data integrity check list is part of the OSPO Code Review Security check lists
ETRAP-R 9.2: The eTRaP system shall comply with OSPO development security check list.
  OSPO development security check list is part of the OSPO Code Review Security check lists
ETRAP-R 9.3: The eTRaP system shall comply with OSPO code check list.
  OSPO code check list is part of the OSPO Code Review Security check lists
74

## Slide 75: Requirements – Summary
The eTRaP Requirements have been established.
The Requirements have been documented in the Requirements Allocation Document (RAD).
The Requirements are traceable to drivers (customer needs or expectations) and other requirements.
75

## Slide 76: System Description Liqun Ma
76
Notes: 76

## Slide 77
Retrieve information about active tropical cyclones.
Retrieve rain rate data from N-18/19/MetOp-A/B, F17/18, GHE, S-NPP/ATMS, GCOM/AMSR2, and GPM/GMI.
Generate 6-hour total Tropical Rainfall Potential (TRaP) for each active storm and each satellite listed above.
For each active storm, generate Ensemble Tropical Rainfall Potential (eTRaP).
Major Components
77
Notes: BK: Capitalized “Tropical Rainfall Potential” in third bullet and “Ensemble Tropical Rainfall Potential” in last bullet

## Slide 78
System Architecture, Data Flow, Security
78
Test
GEOPROD3t
Linux
Distribution via web
GP5 (OSPO web)
Linux
Production
GEOPROD3
Linux
FOS Forecasts (JTWC,,NHC CPHC)
FOS2
Linux
ASCII
ADDE
Pull
Ascii and Tar file
ftp push
McIDAS Area Files: ADDE pull
Distribution via ftp
SATEPSANONE
AIX
N-18/19 /MetOp-A/B MHS MW rain rates
SFS/GEODIST
Development
GEODEV
Linux
DDS/PDA
CM Repository
cm-espc
Linux
DMSP F17/18 SSMI/S
FNMOC MW rain rates
SFS/GEODIST
GHE IRRRs
SFS/GEODIST
External User Zone
Distribution Zone (DMZ)
Development Zone
Production Zone
SATEPS Security at ESPC/NSOF
S-NPP ATMS MW rain rate
SFS/GEODIST
GCOM-W1 AMSR-2 rain rate
SFS/GEODIST
JTWC, NHC,CPHC,
N-18/19 /MetOp-A/B MHS MW Mcidas converter
Polarprod
AIX
DMSP F17/18 SSMI/S
FNMOC MW Mcidas converter
Polarprod
Linux
GHE SATEPSDIST IRRRs
GHE1
Linux
S-NPP ATMS MW Mcidas converter
MGTPROD
Linux
GCOM-W1 AMSR-2 MW Mcidas converter
MGTPROD
Linux
Conversion to McIDAS AREA file format is extrernal to eTRaP processing
GIF sftp push
Ascii, GIF sftp push
WPC
NCEI
Tar file containing GIF, McIDAS Area Files, ASCII
ftp pull
Ascii ftp pull
GPM GMI rain rate
SFS/GEODIST
GPM MGI MW Mcidas converter
MGTPROD
Linux
Storm SHIPS(R-CLIPER)
SFS
Notes: BK: Replaced “HPC” with “WPC”.

## Slide 79
eTRaP is running on ESPC geo system
  Development / Test – Server
    Pre-operational codes (DAP) received from STAR have been thoroughly tested on geoprdo3t at ESPC
  Production – Server
    eTRaP is running on geoprod3.
    The products will be distributed to users through ESPC Data Distribution server (DDS/PDA) and ESPC website server (GP5)
Production
79
Notes: LM: yes. Added. And also change ‘will be runing’ to is running’
BK: Should we mention PDA also?

## Slide 80
Ops Server: Vmware server ‘geoprod3’
  Intel(R) Xeon(R) CPU E7- 4850
  2.00 GHz
  1 GB memory
  RedHat 5.8 64-bit
Libraries installed
  McIDASv2016.1
Hardware / Software
80

## Slide 81
N18/N19, MetopA/B MHS single-orbit rain rates from SFS/geodist
SSMIS (F17/F18) single-orbit rain rates from SFS/geodist
GHE 1HR rain rates accumulations from SFS/geodist
NPP MIRS rain rates from SFS/geodist
GCOM-W AMSR2 rain rates from SFS/geodist
GPM GMI rain rates from SFS/geodist
RSMC bulletins from FOS2
Input Data Sources
81
Notes: LM: delete the question mark. Not sure if GPM/GMI will be on SFS/geodist at first?
BK: Why the question mark in the second-to-last bullet? (FWIW, slide 95 doesn’t have a question mark in the corresponding GMI bullet.)

## Slide 82
TC forecast files (bulletins) are pulled from FOS every ten minutes.
  Tropical cyclone position is extracted from bulletins.
TC Forecast File
82

## Slide 83
Geolocation data for NOAA-18/19 , Metop-A/B and SSMSI F17/18 are generated on ESPC Polarprod and pushed to SFS for eTRaP (binary)
Geolocation data for NPP/ATMS, GCOM/AMSR2, and GPM/GMI are generated on ESPC Linux server MGTPROD and pushed to SFS for eTRaP (binary)
Geolocation data for GHE is generated on ESPC Linux server GHE1 and pushed to SFS for eTRaP (binary)
Those geolocation data are used to check whether any orbital data from any of the above satellites covers the active storm.
Orbit Geolocation Data
(NOAA-18/19, MetOp-A/B, SSMIS F17/18, NPP/ATMS, GCOM/AMSR2, GMI)
83

## Slide 84
Rain rate data for NOAA-18/19 , Metop-A/B and SSMSI F17/18 are converted to McIDAS format on ESPC Polarprod and pushed to geodist for eTRaP
Rain rate data for NPP/ATMS , GCOM/AMSR2 and GPM/GMI are converted to McIDAS format on ESPC Linux server MGTPROD and pushed to SFS for eTRaP
Rain rate data from GHE are generated on ESPC Linux server GHE1 and pushed to geodist for eTRaP
Those rain rate data are used to generate 6-hour total Tropical Rainfall Potential (TRaP) for each active storm.
TraPs from each satellite are used to generate ensemble Tropical Rainfall Potential (eTRaP) for each active storm.
Orbit Rain Rate Data
(NOAA-18/19, MetOp-A/B, SSMIS F17/18, NPP/ATMS, GCOM/AMSR2, GMI)
84
Notes: BK: changed “satellites” to “satellite in last bullet

## Slide 85
Generate TRaPs
  Search FOS for active storms
  For each active storm, loop thorough each satellite orbits to search for orbits that cover the storm and within 6 hours of forecast time.
  Get the orbit rain rate data and generate 6-hr TRaPs and 24-hr TRaP.
Product Processing (1/4)
85

## Slide 86
TRaP generator
Get latest TRaP geolocation data
Geolocation data for AMSU/MHS orbit
Geolocation data for SSMIS orbit
Geolocation data for GHE
Geolocation data for ATMS orbit
FOS forecast bulletins
Collect info on all active storms
ADDE
Active storms?
Exit
N
Y
Geolocation data matching storm coverage and time?
N
Run TRaP code for orbits meeting time and location criteria [pctrpauto.pgm]
AMSU/MHS TRaPs
SSMIS TRaPs
GHE TRaPs
ATMS TRaPs
Done
Y
Geolocation data for AMSR2 orbit
AMSR2 TRaPs
R-CLIPER
Exit
Rain Rate for SSMIS orbit
Rain Rate for AMSU/MHS orbit
Rain Rate from GHE
Rain Rate for ATMS orbit
Rain Rate for AMSR2 orbit
Geolocation data for GMI orbit
GMI TRaPs
Rain Rate for GMI orbit
Product Processing (2/4)
86

## Slide 87
Generate eTRaPs
  For each storm, collect all TRaPs for this storm at different time period and generate eTRaP products for this storm in McIDAS format.
  Convert eTRaP product from McIDAS to ASCII and images.
Product Processing (3/4)
87

## Slide 88
eTRaP generator
AMSU/MHS TRaPs
SSMIS TRaPs
GHE TRaPs
ATMS TRaPs
Collect info on all active storms
Active storms?
Exit
N
Collect TRaPs and generate eTRaP products
Y
AMSR2 TRaPs
1.ensemble mean rainfall(6-h and 24-h)
2.probability-matched ensemble mean rainfall(6-h and 24-h)
3.PoP exceeding 25 mm (6-h)
4.PoP exceeding 50mm (6-h and 24-h)
5. PoP exceeding 75mm( 6-h)
6. PoP exceeding 100m (6-h and 24-h)
7. PoP exceeding 150 mm (24-h)
8. PoP exceeding 200 mm (24-h)
McIDAS
eTRaP data format converter
eTRaP product in Ascii and image and tar file
GMI TRaPs
Product Processing (4/4)
88
Notes: BK: Changed “Pop” to “PoP”

## Slide 89: eTRaP – Run Schedule Data Retrieval and Processing
0,10,20,30,40,50 * * * * $HOME/mcidas/pctrap-V3/getpPass.pl > /data/TRAP/log/getpPass.log 2>&1
1,11,21,31,41,51 * * * * $HOME/mcidas/pctrap-V3/pctrap-auto-newTime.pl >> /data/TRAP/log/autoTRAP.log 2>/data/TRAP/log/autoTRAP.err
5 * * * * $HOME/mcidas/etrap/scripts/etrap_mainF.sh > /tmp/etrap.out 2>&1
5 23 * * * $HOME/mcidas/etrap/scripts/createTar_NCDC.sh > /tmp/sendTar_NCDC.log 2>&1
89
Notes: 89

## Slide 90
File | File name | Array Size | Units
Ensemble average accumulated rainfall for 0-6, 6-12, 12-18, 18-24, and 00-24 h (separate files) | AREA file: YYYY<NAME>avgqpf.MMDDHH00.LL, where YYYY is the year, NAME is the storm name, MMDDHH is the initialization month, day, GMT hour, and LL is the time at the beginning of the forecast interval (except 24=24-h forecast). The ASCII file has the same naming convention except with a .TXT at the end. | 800x800 | 6-h accumulations: inches*255/20; 24-h accumulations: inches*255/40.
Probability-weighted accumulated rainfall for 0-6, 6-12, 12-18, 18-24, and 00-24 h (separate files) | AREA file: YYYY<NAME>pmqpf.MMDDHH00.LL. The ASCII file has the sane naming convention except with a .TXT at the end. | 800x800 | Same as above
Probability of exceedence of 25, 50, 75, or 100 mm rainfall accumulation in 6 h (separate files) | YYYY<NAME>pPP(P).MMDDHH00.LL(.TXT) where PP(P) is the threshold value (mm) for the exceedance probability. | 800x800 | Percentage (0-100)
Probability of exceedence of 50, 100, 150, or 200mm rainfall accumulation in 24 h (separate files) | YYYY<NAME>pPP(P).MMDDHH00.24 (.TXT) | 800x800 | Percentage (0-100)
Output Files
90

## Slide 91
Output Files
91

## Slide 92: Outline
Introduction
Risks and Action
System Requirements
System Description
System Test
System Operational Readiness
Summary
92
Notes: 92

## Slide 93: System Test Bob Kuligowski, Robert Glassberg, and Liqun Ma
93
Notes: 93

## Slide 94: System Test - Objectives
Ensure that GPM/GMI TRaPs are generated correctly.
Ensure that GPM/GMI TRaPs are added to eTRaP correctly.
Ensure eTRaP distribution and monitoring systems work correctly.
No Unit test for this enhancement.
94

## Slide 95: System Test - Test Environment
The system test for this eTRaP update was performed on geoprod3t:
  Intel(R) Xeon(R) CPU E7- 4850
  2.00 GHz
  1 GB memory
  RedHat 6.4 64-bit
McIDAS libraries installed
  McIDASv2012.2
95
Notes: Update?

## Slide 96: System Test - Test Datasets
Overall system test is conducted on geoprod3t with all required real-time data, including:
  N18/N19, MetopA/B MHS single-orbit rain rates from SFS/geodist
  SSMIS(F17/F18) single-orbit rain rates from SFS/geodist
  GHE 1HR rainfall accumulations from SFS/geodist
  NPP ATMS MIRS single-orbit rain rates from SFS/geodist
  GCOM-W AMSR2 single-orbit rain rates from SFS/geodist
  GPM GMI single-orbit rain rates from SFS/geodist
  RSMC bulletins from FOS2
96
Notes: BK: Added “GPM” before “GMI” for consistency

## Slide 97: System Test - Test Datasets
  eTRaP is an event-driven product. It was tested with new input data on the following real storms since it was installed on its test server on December 2016:
  01W - Northwest Pacific
  3S - Southeast Indian
  CARLOS- Southwest Indian
  DINEO - Southwest Indian
97
Notes: LM: done
BK: Need to fill in the number in the last bullet

## Slide 98: System Test - Test Items
Production Components
  Get GMI rain rate data and generate GMI TRaPs
  Add GMI TRaPs to eTRaP
Dissemination Components
  DDS – ASCII and tar files
  GP50 – gifs and text logs for Web monitoring
  Since this is just a product upgrade for eTRaP, all dissemination components are unchanged and no test for data distribution.
QC Monitoring Components
  No test for monitoring.
98
Notes: Can you update?

## Slide 99: System Test - Test Configuration
Define input/output locations
  Make sure the input data are all available
  Make sure all output directories are generated
Compile source code
  In ../src, execute ‘make’
  Verify all executable ‘*.exe’ generated and put in ../bin
Prepare scripts
  Test acquisition drivers, process driver, product generation driver, and dissemination scripts individually
  System test of scripts’ interactivity and compatibility on cron daemon
Set up cron table for eTRaP
99

## Slide 100: System Test Results
System Test Results were reviewed by the eTRaP algorithm developer, PAL and eTRaP Programmer
Product output generated from geo test were compared with the same products generated from geo product.
100

## Slide 101: System Test Test Result (without GPM/GMI)—01W
Without GPM/GMI, fewer members to produce eTRaPs for some periods
101
Notes: Changed “less” to “fewer”

## Slide 102: System Test Test Result (with GPM/GMI)—01W
With GPM/GMI, more members to produce eTRaPs for all periods
102

## Slide 103: System Test Test Result—01W
Pop > 25 mm(without GPM/GMI)
Pop > 25 mm(with GPM/GMI)
Additional members improved probability resolution
103
Notes: Changed “more” to “additional”

## Slide 104: System Test Test Result—01W
Pop > 50mm(without GPM/GMI)
Pop > 50 mm(with GPM/GMI)
Additional members improved probability resolution
104
Notes: Changed “more” to “additional”

## Slide 105: System Test – Verification (data)
GMI rain rates were obtained from NASA and stored in STAR at /data/data081/bobk/eTRaP/GMI
      The GMI rain rates were converted from HDF format to McIDAS AREA file format offline and stored in the same directory.
Archive eTRaPs and TRaP members stored in STAR at /data/data081/bobk/eTRaP/SABarchive
Archive Stage IV data for ground-truth validation stored in STAR at /data/data081/bobk/eTRaP/Stage4_data
Four storms that made landfall over the CONUS were selected based on data availability and capture of an entire storm in the scan:
  Ana (2015)—two GMI overpasses
  Colin (2016)—two GMI overpasses
  Julia (2016)—one GMI overpass
  Matthew (2016)—three GMI overpasses
105
Notes: BK: Updated pathnames

## Slide 106: System Test – Verification (Ensemble parameters)
The first step is to determine the two parameters required to integrate a new instrument into the eTRaP ensemble as outlined in Ebert et al. (2009):
  Bias adjustment (SensorBias): the inverse of the volume bias of the TRaPs from the new instrument to those from the baseline instruments;
  Ensemble weight (SensorWeight): the ratio of the Equitable Threat Score of the new instrument to that from the baseline instruments.
    The ETS is computed at a threshold of 12.7 mm for 6-h accumulations and 25.4 mm for 24-h accumulations
106
Notes: BK: Corrected spelling of “Ensemble” in title

## Slide 107: System Test – Verification(Ensemble parameters)
The GMI TRaPs were basically unbiased relative to the other MW TRaPs (within the bounds of confidence for such a small sample size), so a SensorBias of 1 was chosen.
107
Notes: BK: No updates since last version

## Slide 108: System Test – Verification(Ensemble parameters)
The SensorWeight values range from 0.79 to 1.26; a value of 1 was chosen since the difference in ETS was not statistically significant and since SensorWeight cannot vary with lead time.
108
Notes: BK: no updates since last version

## Slide 109: System Test – Verification
Validation of the resulting eTRaP for 18 forecasts for 4 different storms in 2015-16 shows negligible impact on skill—which is fine since increased product reliability is the goal!
109
Notes: BK: no updates since last version

## Slide 110: System test – verification (Example—Matthew (2016))
Comparison of 0-24 h forecasts of rainfall initialized at 12 UTC 8 October 2016
110
eTRaP w/o GMI
eTRaP w/GMI
Stage IV
Stage IV
Notes: BK: No updates since last version

## Slide 111: System Test Processing Monitoring - Operators Needs
No test needed.
Notes: 111
LM: updated.
BK: No test needed or just no test?

## Slide 112: System Test Product Monitoring – QC/QA Needs
No test needed.
112
Notes: 112

## Slide 113: System Operational Readiness Liqun Ma NESDIS/OSPO
113
Notes: 113

## Slide 114: System Operational Readiness: Products
Inputs
  N18/N19, MetopA/B MHS single-orbit rain rates from SFS/geodist
  SSMIS (F17/F18) single-orbit rain rates from SFS/geodist
  GHE 1HR rainfall accumulations from SFS/geodist
  NPP MIRS rain rates from SFS/geodist
  GCOM-W AMSR2 rain rates from SFS/geodist
  GPM GMI rain rates from SFS/geodist
  RSMC bulletins from FOS2
Coverage
  Global
Formats
  McIDAS AREA / ASCII / Binary
Latency
  4 hours
114

## Slide 115
File | File name | Array Size | Units
Ensemble average accumulated rainfall for 0-6, 6-12, 12-18, 18-24, and 00-24 h (separate files) | AREA file: YYYY<NAME>avgqpf.MMDDHH00.LL, where YYYY is the year, NAME is the storm name, MMDDHH is the initialization month, day, GMT hour, and LL is the time at the beginning of the forecast interval (except 24=24-h forecast). The ASCII file has the same naming convention except with a .TXT at the end. | 800x800 | 6-h accumulations: inches*255/20; 24-h accumulations: inches*255/40.
Probability-weighted accumulated rainfall for 0-6, 6-12, 12-18, 18-24, and 00-24 h (separate files) | AREA file: YYYY<NAME>pmqpf.MMDDHH00.LL. The ASCII file has the sane naming convention except with a .TXT at the end. | 800x800 | Same as above
Probability of exceedence of 25, 50, 75, or 100 mm rainfall accumulation in 6 h (separate files) | YYYY<NAME>pPP(P).MMDDHH00.LL(.TXT) where PP(P) is the threshold value (mm) for the exceedance probability. | 800x800 | Percentage (0-100)
Probability of exceedence of 50, 100, 150, or 200mm rainfall accumulation in 24 h (separate files) | YYYY<NAME>pPP(P).MMDDHH00.24 (.TXT) | 800x800 | Percentage (0-100)
System Operational Readiness: Products
output
115

## Slide 116: System Operational Readiness Users of Products
User | POCs | Products | Dissemination
WPC | Mark Klein | 6-hourly | ESPC ftp server / DDS / PDA
NESDIS/SAB | Mike Turk | 6-hourly | ESPC WEB Server
NCDC/CLASS | Philip Johns | daily | ESPC ftp server / DDS / PDA
All other users | All other users | 6-hourly / daily | ESPC Web Server / ftp server
116
Notes: BK: Replaced “HPC/WPC” with “WPC” and added “PDA” alongside the DDS references.

## Slide 117: System Operational Readiness Production Environment
Development – geodev
Testing – geoprod3t
Production – geoprod3
  Upgraded eTRaP will be running to generate the operational products on geoprod3
  eTRaP products are distributed to users through ESPC web server(GP5), DDS / PDA and anonymous ftp server Satepsanone.
Backup – No backup server
117
Notes: BK: Added PDA to go along with DDS

## Slide 118: System Operational Readiness Dissemination
Internet (web Interface)
  No change
DDS/PDA
  No change
Satepsanone
  No change
118
Notes: LM: don’t remember why. Change DDS to DDS/PDA
BK: Why the asterisk after “DDS”; is this because PDA will replace it?

## Slide 119: System Operational Readiness Monitoring
Quality Monitoring
  No change
Performance Monitoring
  No change
119

## Slide 120: System Operational Readiness Operation and Maintenance
O&M Procedures remain the same (no change)
Operational Support remain the same (no change)
120

## Slide 121: System Operational Readiness QA – Code Standards
The eTRaP operational team has been working with the development team to ensure that the upgraded eTRaP follows ESPC operational requirements / guidance:
  Directory structures
  File/directory naming conventions
  Operational log file content
  Error tracking and handling
121

## Slide 122: System Operational Readiness QA – CM and IT security
Product Implementation
  Implementation on parallel test environment and transition to operation are tasked and managed by CRs (WR1805 and CCR3833) through OSPO Enterprise Configuration Management Tool (ECMT)
  Software CM follows ESPC Software Configuration Management Process and Procedures Manual
  Related code and scripts will be checked into subversion
Security Procedures
  This upgraded eTRaP is being tested in a separate test environment (geoprod3t) before installation in operational environment (geoprod3)
  SIA will be performed for this eTRaP upgrade before the system is promoted into operations
Documents will be under the CM control at OSPO
  G:\Common\ESPC Library
122

## Slide 123: System Operational Readiness QA – Documentation
Interface Control Document(ICD) will be updated.
All other documentations remain the same (no change)
123

## Slide 124: System Operational Readiness Archive
  eTRaP products (tar file) will continue being archived at CLASS.
124

## Slide 125: System Operational Readiness User Readiness (1 of 2)
Data Access
  Data access remains the same (no change)
Acceptance of Product
  WPC and SAB already using eTRaP since 2009
125
Notes: BK: Deleted “HPC”.

## Slide 126: System Operational Readiness User Readiness (2 of 2)
Training
  User manuals are available to all users
  WPC/SAB
    No specific training from OSPO is required. Users have been using current eTRaP Since July 2009. This eTRaP upgrade is just an enhancement.
  ESPC Operator
    Monitoring eTRaP will be the same as current eTRaP. No training is needed for ESPC help desk.
126
Notes: Replaced “HPC/WPC” with “WPC”.

## Slide 127: System Operational Readiness Summary
The product system is ready for operations
The documentation will be complete by the time the eTRaP Upgrade is officially declared operational (final touches need to be done to the documents)
The users are ready to receive and use the data
127

## Slide 128: Summary Liqun Ma NESDIS/OSPO
128
Notes: 128

## Slide 129: Summary
Risk and Actions have been reviewed
Requirements and their Allocations have been reviewed
System Description and Test have been reviewed
Products Quality Readiness have been reviewed
Operation Readiness has been reviewed
User Readiness has been reviewed
129
Notes: 129

## Slide 130: Next Steps
Operational Phase
    SPSRB Decision Briefing – March 2017
    Operational Commencement – April 2017
130
Notes: 130

## Slide 131: Open Discussion
The review is now open for free discussion
131
Notes: 131