## Slide 1: Advances in Taylor Oil Spill Detection from Non-SAR Satellite: An Preliminary Analysis
Wei Li1, Banghua Yan2, Nan Chen1,
Yongzhen Fan1, Ellen Ramirez3, Dingkun P. Yan
(SAB Intern)3,4, and Davida Streett3
Stevens Institute of Technology 2. NESDIS/STAR/Satellite Calibration and Data Assimilation 3. VA W.T. Woodson High School 4. OSPO/SPSD/Satellite Analysis 5. NJ Union County Magnet High School

## Slide 2: Background: MODIS Terra Case Study
Location: Taylor Energy Oil Platform
Oil spill can be easily detected by human eye when there is sun-glint exist.
Example: RGB image
T20110612
T20130617
T20160508
(Detected by OSPO/SAB Oil Team)

## Slide 3: Can It Be Detected Automatically Using Non-SAR Satellite Observations?
Oil reflectance is always higher than sea water
The water reflectance will quickly decrease with the wavelength increase, even under the sun-glint situation, while oil has relative flat reflectance over visible and NIR wavelength range
Chart: Oil and Water Reflectance Statistics
| 469 | 555 | 645 | 859 | 1240 | 1640 | 2130
Ave. (Oil) | 0.2206 | 0.2109 | 0.2046 | 0.2111 | 0.2023 | 0.1954 | 0.1663
Ave. + Std. (Oil) | 0.2466 | 0.2417 | 0.23493 | 0.2388 | 0.2269 | 0.2171 | 0.1856
Avg. - Std. (Oil) | 0.1946 | 0.1801 | 0.17427 | 0.1834 | 0.1777 | 0.1737 | 0.147
Ave. (Water) | 0.1855 | 0.1717 | 0.1626 | 0.1643 | 0.159 | 0.154 | 0.1297
Ave. + Std. (Water) | 0.1937 | 0.18294 | 0.1736 | 0.1743 | 0.17034 | 0.1639 | 0.1392
Ave. - Std. (Water) | 0.1773 | 0.16046 | 0.1516 | 0.1543 | 0.14766 | 0.1441 | 0.1202

## Slide 4: Threshold Method
NDOI: Normalized Difference Oil Index.
NDOI = (R469-R859)/(R469+R859)
R555 > 1
NDOI < 2

## Slide 5: Threshold Method: Example 1 (20110612)
Case: T20110612
RGB image
Normalized R at 555 nm
NDOI
Oil feature detected
Oil thresholds:
R555 > 0.3
NDOI < 0.15

## Slide 6: Threshold Method: Example 2 (20130617)
Oil thresholds:
R555 > 0.2
NDOI < 0.015
Normalized R at 555 nm
Oil feature by threshold

## Slide 7: Threshold Method: Example 3 (20160508)
Oil thresholds:
R555 > 0.2
NDOI < 0.048
Normalized R at 555 nm
Oil feature by threshold

## Slide 8: Challenge
  The threshold values will change case by case due to the sun-glint intensity under different solar/viewing angles, wind as well as oil type.

## Slide 9
  Can we simulate the reflectance from oil and water and use machine learning techniques to identify them?
  Oil and water have different refractive indices in visible and NIR. The higher refractive Index of oil will result in larger surface reflectance. From literature we find the refractive index of oil varies with oil type and we used 1.38 -1.46 range in this test. The refractive index of water is tabulated from Segelstein 1981.
Our Thought

## Slide 10: Ocean Surface Reflectance Modeling

## Slide 11: Rough Surface in DISORT3 Model

## Slide 12: Validation Result by NASA CAR Measurement
MODEL
MEASUREMENT
MODEL
MEASUREMENT

## Slide 13: RT Model Simulation Design
During sun-glint, the signal received from satellite comes mostly from water surface, the water leaving radiance can be ignore.
We setup a rough surface model to simulate the water and oil sun-glint reflectance in MODIS channels, separately. Then we mix the reflectance of oil and water cases by assuming the fraction of oil (fraction = 1 is oil, fraction=0 is water).
We generated 50,000 cases for oils and water separately, to cover the possible solar and satellite viewing angle in sun-glint area, as well as wind speed range from 0 to 10m/s.
The multi-layer neural network (MLNN) was used to train these 50,000 cases. Using the trained net, we can find the fraction from the satellite measured radiance and wind speed.
We assume the oil refractive index is from 1.38 to 1.46.

## Slide 14: Retrieval Flowchart
RT model
Geometry angles
Wind speed
Refractive index(water, oil)
50,000 mixed R with oil fraction f
R = f*R_o + (1-f)*R_w
R_w:
simulated MODIS water reflectance
R_o:
simulated MODIS oil reflectance
MLNN train
Geometry angles
Wind speed
Refractive index(water, oil)
MODIS measurement
wind speed
net
Oil fraction f

## Slide 15: Threshold and Automatic Oil Detection Comparison: Example 1
Case: T20110612
Normalized R at 555nm
Oil feature by threshold
Oil feature by MLNN

## Slide 16: Threshold and Automatic Oil Detection Comparison: Example 2
Oil feature by threshold
Oil feature by MLNN
Normalized R at 555 nm

## Slide 17: Threshold and Automatic Oil Detection Comparison: Example 3
Oil feature by threshold
Oil feature by MLNN
Normalized R at 555 nm

## Slide 18: Threshold and Automatic Oil Detection Comparison: Example 4
Oil feature by MLNN
Normalized R at 555 nm
Oil feature by threshold

## Slide 19: Threshold and Automatic Oil Detection Comparison: Example 5
20140503
Normalized R at 555 nm
Oil feature by threshold
Oil feature by MLNN

## Slide 20: Summary
One threshold method has been developed to detect Taylor oil spills using MODIS Terra observations of reflectance:
    NDOI = (R469-R859)/(R469+R859)
    R555 > 1
    NDOI < 2
  where 1 and 2 vary with sun-glint intensity, wind speed, and oil type.
An automatic oil detection method is further developed by using multi-layer neural network (MLNN) with Radiative transfer model simulation.
  The preliminary results show that this automatic oil detection algorithm works very well and can detect major oil spill features.
  More studies are need to finalize the algorithm.

## Slide 21: References
Fan, Y., Li, W., Gatebe, C.K., Jamet, C., Zibordi, G., Schroeder, T., and Stamnes, K., (2017) “Atmospheric correction and aerosol retrieval over coastal waters using multilayer neural networks”, submitted to Remote Sensing of Environment.
Y. Fan, W. Li, K. J. Voss, C.K. Gatebe, and K. Stamnes, (2016), A neural network method to correct bidirectional effects in water-leaving radiance, Appl. Opt., 55(1):10-21, DOI: 10.1364/AO.55.000010. Z
Z. Lin, W. Li, C. Gatebe, R. Poudyal, and K. Stamnes. (2016), Radiative transfer simulations of the two-dimensional ocean glint reflectance and determination of the sea surface roughness. Appl. Opt., 55(6):1206–1215.
T. Tanikawa, W. Li, K, Kuchiki, T. Aoki, M. Hori, and K. Stamnes, (2015), Retrieval of snow physical parameters by neural networks and optimal estimation: case study for ground-based spectral radiometer system, Optics Express 23(24), DOI: 10.1364/OE.23.0A1442.
Z. Lin, S. Stamnes, Z. Jin, I. Laszlo, S.-C. Tsay, W. Wiscombe, and K. Stamnes, (2015), Improved discrete ordinate solutions in the presence of an anisotropically reflecting lower boundary: upgrades of the DISORT computational tool, J. Quant. Spectrosc. Radiat. Transfer 157, 119–134.